M30 Upgrade Guide

# TFTP Upgrades

- Connect debugging serial device port to PC serial port by serial connection cable ：

- Unplug the motherboard from the chassis :Unscrew the screws on both side of the motherland which faces the side of chassis cable side

Figure 1 as below：

Figure 1

b. Then connect serial connector to the debugging serial port，Figure 2 as below:

Figure 2

- Enable the device to access network, run the corresponding serial port software :“minicom” or “SecureCRT” on the PC, quickly press “*”(within 3 seconds) three times consistently when screen shows “Hit any key to stop autoboot ” and goes to upgrade interface,Figure3 as below

Figure 3

- Setup TFTP server IP  address and device IP address, serial port order is :

Device IP Address:       TI8168_EVM# setenv ipaddr 172.9.2.199

Gateway Address:            TI8168_EVM# setenv gatewayip 172.9.0.1

Subnet Mask：           TI8168_EVM# setenv netmask  255.255.255.0

TFTP Server IP Address: TI8168_EVM# setenv serverip 10.33.9.14

Save modified environment variables:  TI8168_EVM# saveenv

Figure 4 show as below：

Figure 4

- Open TFTP files，Click TFTPServer.exe，弹出如下对话框will show the dialog box as Figure 5；

Figure 5

- Click follower button(indicated by red in Figure 5,6) TFTP interface，will indicate the dialog as Figure 6：

Figure 6

- Click “browse” button in TFTP server interface，select the upgraded file in the right document，Click “Confirm”，then the root of upgrade file is displayed in the function box，upgrade file includes：romfs-x.cramfs.img、 custom-x.cramfs.img、web-x.cramfs.img；

Figure 7

- After clicking confirm，type the order in the serial port software for upgrade firmware is:

a.Run ”run dr” to upgrade “romfs -x.cramfs.img”:   TI8168_EVM# run dr

b.Run ”run dw” to upgrade “web-x.cramfs.img”:    TI8168_EVM# run dw

c.Run “run  dc” to upgrade custom-x.cramfs.img:     TI8168_EVM# run dc

d.Setup environment variables：

TI8168_EVM# set bootargs "mem=172M console=ttyO0,115200n8 rootfstype=cramfs root=/dev/mtdblock1 notifyk.vpssm3_sva=0xBFD00000 pcie=x2,gen2"

e.Save environment variables：                         TI8168_EVM# save：

See Figure 8 as below

Figure 8

When the screen show“write: 100%  done”notification，it means “romfs-x.cramfs.img” upgrade successfully。（Attention： Due to the front panel has the watchdog，the upgrade process has not been completed 100%，it may reboot, and press “*” three times quickly after reboot，and goes to run dr again，this situation is also the same to “run dc” 、”run dw”，until it shows“write: 100%  done”）

- When the upgrade is complete，close the TFTP Server and serial port device, shut down the power and restart 。

- Please use the WEB client way to upgrade the firmware after the above steps which is for upgrade FPGA process.

# WEB Client Upgrades

- Login the WEB interface by browser。

- Enter “Setup”—“System Setup”—System Upgrade。

- Select MPU to click“Import”button，pop-up “Select File” dialog，the selected similar name is ：“General_DSC_3U_MB_Chn_V2.000.0000.x.R.XXXX.BIN” or “General_DSCON1000_V2.000.0000.0.x.R.XXXX.BIN”，then click “Upgrade” button。

- When the firmware upgrade successfully, it will restart automatically. Refresh the WEB interface and re-login after restart.

Appendix：

1. Default IP Address： 192.168.1.2

2. Setup IP address order under Linux System：

IP：ifconfig eth0 192.168.1.2  netmask 255.255.255.0;

Gateway： route add default gw 192.168.1.1;