Four-Door Access Controller User’s Manual

V1.0.0

Table of Contents

1 Overview	1

2 Device Appearance	2

3 Device Installation and Uninstallation	3

3.1 Device Installation	3

3.2 Device Uninstallation	4

4 Port	6

4.2 Cabling	7

4.3 System Structure	9

5 Technical Specification	11

Important Safeguards and Warnings

Please read the following safeguards and warnings carefully before using the product in order to avoid damages and losses.

Note:

Do not expose the device to lampblack, steam or dust. Otherwise it may cause fire or electric shock.

Do not install the device at position exposed to sunlight or in high temperature. Temperature rise in device may cause fire.

Do not expose the device to humid environment. Otherwise it may cause fire.

The device must be installed on solid and flat surface in order to guarantee safety under load and earthquake. Otherwise, it may cause device to fall off or turnover.

Do not place the device on carpet or quilt.

Do not block air vent of the device or ventilation around the device. Otherwise, temperature in device will rise and may cause fire.

Do not place any object on the device.

Do not disassemble the device without professional instruction.

Warning:

Please use battery properly to avoid fire, explosion and other dangers.

Please replace used battery with battery of the same type.

Do not use power line other than the one specified. Please use it properly. Otherwise, it may cause fire or electric shock.

Special Announcement

This manual is for reference only.

All the designs and software here are subject to change without prior written notice.

All trademarks and registered trademarks are the properties of their respective owners.

If there is any uncertainty or controversy, please refer to the final explanation of us.

Please visit our website for more information.

# 1 Overview

The access controller is a controlling device which compensates video monitoring and bidirectional talk. It has neat and modern design with strong functionality, suitable for commercial building, corporation property and intelligent community.

It has:

- It adopts slideway and lock installation design for easy installation and repair.

- It integrates alarm, access control, video monitoring, fire alarm and control module input.

- It supports 4 sets of card readers.

- It supports 9 groups of input signal (unlock button *4, door sensor *4, intrusion alarm *1).

- It supports 5 groups of output control (electric lock *4, alarm output *1).

- RS485 port, may extend to connect to lift control module, alarm or household control module. It may connect upper device via RS485.

- FLASH storage capacity is 16M (may extend to 32M), max supports 100,000 card holders and 150,000 records.

- It supports illegal intrusion alarm, unlock overtime alarm, forced card alarm and forced setup. It also supports black-white list and patrol card setup

- It supports setup of card period, password and validity. Guest card in additional has setup of times of use.

- It supports 128 groups of schedules, 128 groups of periods and 128 groups of holiday schedule.

- Data storage during outage, built-in RTC (support DST), online upgrading.

# 2 Device Appearance

Access controller appearance and dimension are shown in Figure 2- 1 Dimension 1 and Figure 2- 2 Dimension 2. Unit is mm.

Figure 2- 1 Dimension 1

Figure 2- 2 Dimension 2

# 3 Device Installation and Uninstallation

## 3.1 Device Installation

You can install the device either:

- Fix it on wall with screw.

- Fix it on wall with bracket.

Installation 1: Fix device on wall with screw as in Figure 3- 1

Figure 3- 1

Installation 2: Fix it on wall with bracket as in Figure 3- 2.

Figure 3- 2

Installation steps:

- Fix bracket on wall with screw.

- Fasten the device into slot on bracket and pull device downward until it is in place.

## 3.2 Device Uninstallation

Uninstallation method for installation 2 is shown in Figure 3- 3.

Figure 3- 3

Uninstallation method:

- Face screwdriver toward the slot and press it to fasten.

- Do it again for second slot, and you can take the device down.

# 4 Port

Device ports are illustrated in Figure 4- 1.

Figure 4- 1

Ports are defined as:

| No. | Port | No. | Port |
| --- | --- | --- | --- |
| 1 | RS485 communication, software port | 8 | TCP/IP, software platform port |
| 2 | No.1, 2 doors unlock +door sensor | 9 | No.1 door card reader |
| 3 | No.3, 4 doors unlock +door sensor | 10 | No.2 door reader |
| 4 | Alarm input/output | 11 | No.3 door reader |
| 5 | No.1, 2 doors lock control output | 12 | No.4 door reader |
| 6 | No.3, 4 doors lock control output | 13 | Reset |
| 7 | Dial-up switch | 14 | DC 12V power port |

Indicators are defined as:

| No. | Note |
| --- | --- |
| 15 | Lock status indicator |
| 16 |  |
| 17 |  |
| 18 |  |
| 19 | Power indicator |

## 4.2 Cabling

Cabling ports of No.1 to 7 are shown as Figure 4- 2.

Figure 4- 2

Cabling ports of “RS485 communication” are as follows:

| Port | No. | Cabling Port |
| --- | --- | --- |
| 485 Communication | 1 | GND |
|  | 2 | GND |
|  | 3 | 485- |
|  | 4 | 485+ |

Cabling ports of “Unlock+Door sensor” are as follows:

| Port | No. | Cabling Port | Note |
| --- | --- | --- | --- |
| Unlock+Door Sensor | 5 | PUSH1 | No.1 door’s unlock button |
|  | 6 | GND | No.1 door’s unlock button and door sensor |
|  | 7 | SR1 | No.1 door’s door sensor |
|  | 8 | PUSH2 | No.2 door’s unlock button |
|  | 9 | GND | No.2 door’s unlock button and door sensor |
|  | 10 | SR2 | No.2 door’s door sensor |
|  | 11 | PUSH3 | No.3 door’s unlock button |
|  | 12 | GND | No.3 door’s unlock button and door sensor |
|  | 13 | SR3 | No.3 door’s door sensor |
|  | 14 | PUSH4 | No.4 door’s unlock button |
|  | 15 | GND | No.4 door’s unlock button and door sensor |
|  | 16 | SR4 | No.4 door sensor |

Cabling ports of “Alarm Input/Output” are as follows:

| Port | No. | Cabling Port | Note |
| --- | --- | --- | --- |
| Alarm Input/Output | 17 | ALA-IN | Alarm input |
|  | 18 | GND- |  |
|  | 19 | OUT+ | Alarm output |
|  | 20 | OUT- |  |

Cabling ports of “Lock output control” are as follows:

| Port | No. | Cabling Port | Note |
| --- | --- | --- | --- |
| Lock Control Output | 21 | NC1 | No. 1 door outage unlock |
|  | 22 | COM1 | No. 1 lock power 12V input |
|  | 23 | NO1 | No. 1 door outage lock off |
|  | 24 | NC2 | No. 2 door outage unlock |
|  | 25 | COM2 | No. 2 lock power 12V input |
|  | 26 | NO2 | No. 2 door outage lock off |
|  | 27 | NC3 | No. 3 door outage unlock |
|  | 28 | COM3 | No. 3 lock power 12V input |
|  | 29 | NO3 | No. 3 door outage lock off |
|  | 30 | NC4 | No. 4 door outage unlock |
|  | 31 | COM4 | No. 4 lock power 12V input |
|  | 32 | NO4 | No. 4 door outage lock off |

Cabling ports of card reader are shown in Figure 4- 3.

Figure 4- 3

Cabling ports of “No. 1 entry card reader” are as follows. It is same for “No.1 door’s card reader”, “No.2 door’s card reader”, “No.3 door’s card reader” and “No.4 door’s card reader”.

| Port | No. | Cabling Port | Note |
| --- | --- | --- | --- |
| No.1 Entry Card Reader | 1 | 485+ | 485 card reader |
|  | 2 | 485- |  |
|  | 3 | LED | Wiegand card reader |
|  | 4 | D0 |  |
|  | 5 | D1 |  |
|  | 6 | CASE |  |
|  | 7 | GND | Card reader power |
|  | 8 | 12V |  |

4 RJ45 cables’ colors are defined as follows:

| No. | Cabling Port | Color |
| --- | --- | --- |
| 9 | 485+ | White-orange |
|  | 485- | Orange |
|  | LED | White-green |
|  | D0 | Blue |
|  | D1 | White-blue |
|  | CASE | Green |
|  | GND | White-brown |
|  | 12V | Brown |

## 4.3 System Structure

The access controller, lock, card reader and etc. combine a system as in Figure 4- 4.

Figure 4- 4

# 5 Technical Specification

| Parameter | Specification |
| --- | --- |
| Processor | 32 bit ARM processor |
| Storage Capacity | 16M |
| Max User | 100,000 |
| Max Record | 150,000 |
| Card Reader Communication Port | Wiegand, RS485 |
| Platform Communication Port | TCP/IP, RS485 |
| Input Card Reader Quantity | 4 groups |
| Working Power | Rated power 10-15VDC, rated current 0.75A |
| Schedule | 128 |
| Period | 128 |
| Holiday | 128 |
| Unlock Mode | Card, card+password, password, card or password, card+fingerprint, fingerprint+password, fingerprint or card or password, by period. |
| Cross-segment Network | Support |
| Dual-door Lock | Support |
| Real-time Monitoring | Support |
| Alarm Activation | Support |
| Vandal-proof Alarm | Support |
| Illegal Intrusion Alarm | Support |
| Unlock Overtime Alarm | Support |
| Forced Card and Password Setup | Support |
| DST and Time Sync | Support |
| Online Upgrading | Support |

Note:

- This manual is for reference only. Slight difference may be found in user interface.

- All the designs and software here are subject to change without prior written notice.

- All trademarks and registered trademarks are the properties of their respective owners.

- If there is any uncertainty or controversy, please refer to the final explanation of us.

- Please visit our website or contact your local service engineer for more information.