CHAPTER 2

GENERAL DESCRIPTION

The EH-1601 Hub is a standard Ethernet concentrator that retimes and re-transmits the signal to each network station on the LAN. Each Hub has seventeen modular RJ-45 STP ports, one BNC port, one AUI for attaching network devices (file server, bridge, and workstations) or  additional concentrators.

The Cover Panel of EH-1601

On the cover panel of this Hub, there are Power, BNC, AUI and Collision LED. For each RJ-45 STP port, there is a LED indicators - LINK/TX and Receiving . These LEDs help in diagnosing line troubles and indicate the status of data transmission.

Figure 2-1 Cover Panel of EH-1601

For the LEDs indicating the global status are:

1.	Power (Green): The Power LED "lights" if the power "ON".

2.	Collision (Red): The LED "lights" if any collision detected in any port.

For  each port, including BNC and AUI port, the LEDs show the same status.

Each LED is normally OFF after the power on operation, but will light up when this port is correct connected by a station. That means when LED steadily light up, the corresponding