CHAPTER 3

INSTALLATION

Getting Ready to Install the EH-1601

Before installing the EH-1601 Hub, you should determine the installation location.

Make sure that the RJ-45 cable distance between the concentrator and the host device is not longer than 328 feet including all connection cables. Check if you are using a external AC power adapter, 9~15 V DC output, 1A maximum required.

Warning :

Please make sure you are using a power adapter of the right type; otherwise, the warranty will be invalidated.

Make sure there is enough room to service the Hub and to make cable connections to the rear panel.

Avoid direct sunlight, heat vents and warm air exhaust from other equipment.

Installing the Hub

You can place the Hub on a desktop or mount it on the wall.

The wall-mounting design provides space-saving and flexibility in cable routing and expansion. Screws two flat screw onto the wall, and then fix the EH-1601 onto the wall, as Figure 3-1.

Figure 3-1 Mounting EH-1601 on the wall

Follow the steps below to attach the power adapter to the Hub:

1. Insert the jack end of the power adapter into the power port of EH-1601.

2. Insert the plug end of the power adapter into a grounded power outlet.

Now, the Power LED indicator on the front panel of the Hub should be lit. If this LED is still off, check the cable connection, or refer to Chapter 4, "Troubleshooting".

If you want to power off the Hub, unplug the power adapter from the grounded power outlet.

Linking Ethernet Nodes to the Hub

You can connect a workstation or file server to the EH-1601 Hub through the AUI port, BNC port or STP port.

Connection through STP Ports

1. Insert one end of the STP/UTP cable to any STP port of the Hub.

2. Insert the other end of the STP/UTP cable to the STP/UTP port of  the PC node..

Connection through the BNC Port

1. Connect a T-connector to the BNC port of the Hub and one to the BNC port of the workstation or file server.

2. Connect one end of a thin coaxial cable to the T-connector on the BNC port of the  Hub.

3