NOVASwitch

FNSW-800

100Base-TX

Fast Ethernet Switching Hub

Trademarks

Copyright ( PLANET Technology Corp. 1998.

Contents subject to revision without prior notice.

PLANET is a registered trademark of PLANET Technology Corp.  All other trademarks belong to their respective owners.

FCC Warning

This equipment has been tested and found to comply with the limits for a Class A digital device, pursuant to Part 15 of the FCC Rules.  These limits are designed to provide reasonable protection against harmful interference when the equipment is operated in a commercial environment.  This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the Instruction manual, may cause harmful interference to radio communications.  Operation of this equipment in a residential area is likely to cause harmful interference in which case the user will be required to correct the interference at his own expense.

Before Starting

In this User's Manual "NOVASwitch" is used for any/all of the PLANET NOVASwitch models of switching hubs listed on the title page. Important differences between models will be specified.

Reversion

PLANET NOVASwitch User's Manual
For Models: FNSW-800

Part No.: EMFNSW800

TABLE OF CONTENTS

1.	UNPACKING INFORMATION	5

2.	PRODUCT INTRODUCTION	7

2.1	Key Features	7

2.2	Front Panel	7

2.2.1	Ports Speed	8

2.2.2	Cabling	8

2.2.3	Status LEDs	9

2.3	The Rear Panel	10

2.3.1	Extension Slot	10

2.3.2	Reset Switch	10

2.3.3	Power Connector	10

2.3.4	Power Switch	10

2.3.5	Fan	11

3.	InstallATION	13

3.1	Rack-Mount Installation	13

3.2	Desktop Installation	13

4.	OPTIMIZING CONFIGURATION	15

4.1	Prior to Installation	15

4.2	Half- and Full-Duplex	15

4.3	Fast Ethernet	16

4.4	Auto-Negotiation	17

4.5	MAC Address Table	17

4.6	Sample Application	18

5.	Troubleshooting	19

6.	PRODUCT SPECIFICATIONS	21

7.	RJ-45 Pin AssignmeT	22

7.1	Straight-Through/Crossover Cable	22

# UNPACKING INFORMATION

Thank you for purchasing a PLANET NOVASwitch switching hub. Before continuing, please check the contents of the product package. This product package should contain the following items:

- One NOVASwitch FNSW-800 Switching Hub

- One Power Cord

- Two Rack-Mounting Brackets with Attachment Screws

- This User’s Guide

Please inform your local dealer/supplier immediately if any item is found to be defective, damaged or missing. Retain the original packaging (carton), including the packing materials, and use them to re-pack the product in the unlikely event there is a need to return it to us for repair.

.

# PRODUCT INTRODUCTION

NOVASwitch FNSW-800 switching hubs are multi-speed, versatile network devices combining both standard and "Big-Pipe" ports under the same hood.

## Key Features

- Compliant with IEEE802.3 and 802.3u standards for 100Base-TX/FX.

- 8-port Fast Ethernet switching hub, pure 10/100Base-TX

- Wire-speed "Store-and-Forward" filtering/forwarding eliminates bad data packets with minimal delay

- 100Base-TX ports automatically sense and set optimal line speed from 10/20, 100/200Mbps, All 100Base-TX port support MII Auto-Negotiation function

- Optional Fiber-optic module for 100Base-FX, shared with port#8. DIP switch for Half/Full-Duplex selection

- Shared buffer memory and up to 12000-entry MAC source address table make for fast handling of data packets

- Internal, full-range power supply suitable for worldwide use

## Front Panel

Figure 1: Front View of the FNSW-800

### Ports Speed

#### ( 100Base-TX

All 100Base-TX ports come with auto-negotiation capability. They automatically support 100Base-TX and 10Base-T networks. Users only need to plug a working network device into one of the 100Base-TX ports, then turn on the hub. The port will automatically runs in 10Mbps, 20Mbps, 100Mbps or 200Mbps after the negotiation with the connected device.

#### ( 100Base-FX

The port 8 can be a 100Base-FX fiber-optic port as the extension module installed (rear). The Half-/Full-Duplex is selectable by the DIP-switch on the module. Please refer to the installation guide of the extension module for more.

### Cabling

NOVASwitch 100Base-TX ports use RJ-45 sockets -- similar to phone jacks -- for connection of unshielded twisted-pair cable (UTP). The IEEE 802.3u Fast Ethernet standard requires Category 5 UTP for 100Mbps 100Base-TX. 10Base-T networks can use Cat.3, 4, or 5 UTP (see table A)

| Port Type | Cable Type | Connector |
| --- | --- | --- |
| 10Base-T | Cat 3, 4, 5 | RJ-45 |
| 100Base-TX | Cat.5 UTP only | RJ-45 |
| 100Base-FX* | 62.5/125(m multi-mode fiber | ST / SC |

Table A: FNSW-800 Model/Port List

### Status LEDs

One green LED to show power On/Off is on the front panel. Also, each port has eight status LED indicators, as shown below.

| Label | Status | Function |
| --- | --- | --- |
| 100 | Steady lit | Lit to indicate that a valid physical UTP/STP connection exists on that port runs in 100Mbps |
| 10 | Steady lit | Lit to indicate that a valid physical UTP/STP connection exists on that port runs in 10Mbps |
| FD | Steady lit | Lit to indicate Full-Duplex mode detected on that port |
| HD | Steady lit | Lit to Indicate Half-Duplex mode detected on that port |
| TX | Blink | Blink to indicate the port is transmitting |
| RX | Blink | Blink to indicate the port is receiving |
| LINK | Steady lit | Lit to indicate a valid physical UTP/STP connection exists on that port |
| COL | Blink | Blinks if a collision is detected when the port is in Half-Duplex mode. |

Table B: FNSW-800 Port-LED Functions

## The Rear Panel

Figure 2: Rear View of FNSW-800

### Extension Slot

FNSW-800‘s port #8 can be a 100Base-FX port switching port as the extension module installed

Please refer to the Installation Guide of the module for the detailed installation and settings.

NOTE: While powering on, FNSW-800 detects the DIP-switch status of the module, then shown on the front panel LED indicators

### Reset Switch

The Reset Switch is located on the left of the rear panel next to the extension slot. Push then releases the button will resets the device. The reset button could be used when the MAC address table needs to be rebuilt.

### Power Connector

The Power Connector is designed to be used with the power cord included in the product package. Attach the female end of the cord to the power connector and the male end of the cord to a grounded power outlet. The accepted power range is from 90VAC to 250VAC, 50/60Hz.

### Power Switch

The power On/Off Switch is located on the right of the rear panel next to the power connector.

### Fan

All computing and communications devices work best when not overheated. Please keep the fan area clear so that the cooling function is not impaired.

# InstallATION

The NOVA Switch models FNSW-800 do NOT require software configuration.  Users can immediately use any of the features of this product simply by attaching the cables and turning on the power.

To get the best use of these NOVASwitch models, many things need to be considered first. See Section 4, OPTIMIZING CONFIGURATION for details.

## Rack-Mount Installation

Most users prefer to attach the power cord to the hub before installation in a network rack. Do not plug the other end of the cord into a power outlet until after the hub is installed.

For mounting the NOVASwitch  in a network rack, first attach the rack-mount brackets to the side of the hub with screws. (Both brackets and screws are included in the product package.) Slide the hub into the rack and align the holes in the bracket with the corresponding holes in the network rack. Attach the bracket to the rack with the enclosed screws.

## Desktop Installation

To locate the NOVASwitch models on a desktop, first attach the four rubber feet to the bottom of the hub, one in each corner. Place the hub on a clean, flat desk or table-top close to a power outlet. Make sure there is no hindrance behind the fan of the hub

Plug in all network connections and the power cord, then turn the switch on.

# OPTIMIZING CONFIGURATION

## Prior to Installation

Before installing the NOVASwitch models and connecting network devices, it is important to plan the new network layout. Consider:

- Dedicated Bandwidth: File servers and other high-traffic hardware can improve if they have their own direct connection with dedicated 10 or 100Mbps bandwidth.

- Full-Duplex: Determine which devices would benefit from a Full Duplex connection and check that they support it.

- Fast Ethernet: 100Base-TX and 100Base-FX have different rules for cable and distance. Make sure these are followed.

- Auto-Negotiation: Devices with different speeds may be easily swapped when the other end of the cable is fixed to a port with auto-negotiation.

- Crossover Uplink: Another hub can be attached to FNSW-800 models using UTP Crossover function.

## Half- and Full-Duplex

The NOVASwitch support both Half- and Full-Duplex modes for 10Base-T, 100Base-TX, and 100Base-FX. Half-Duplex mode is the traditional data transfer mode: one station sends data while other devices wait for the first to finish.

Full-Duplex is the simultaneous transmission and receiving of data. It is only possible between two devices with a dedicated link (e.g., switch-to-switch, switch-to-PC). Both of the devices must be capable of, and set to, Full-Duplex

The 100Base-FX port set Half- or Full-Duplex mode through module's DIP-switch. 100Base-TX ports use auto-negotiation to detect and set the line's operating mode.

## Fast Ethernet

100Base-TX and 100Base-FX are called "Fast Ethernet." This is because they use the Ethernet CSMA/CD access rules and data packet structure, but data travels ten times faster (100Mbps) than traditional 10Mbps Ethernet.

Below is a list of the cable types and connectors supported by FNSW-800 models for 10Base-T, 100Base-TX, and 100Base-FX networks.

| PORT TYPE | Cables Type | Connector |
| --- | --- | --- |
| 100Base-TX | Cat. 5 UTP only | RJ-45 |
| 10Base-T | Cat.3, 4, 5 UTP | RJ-45 |

Table C: Cables & Connectors Supported by FNSW-800

In many cases, 10Base-T LANs can quickly and easily upgrade to 100Base-TX networks. Also, 100Base-FX will become more popular due to its longer range. Table  lists the maximum Fast Ethernet connection distances.

| Max. Link Distance | Copper | Copper+Fiber² | Fiber |
| --- | --- | --- | --- |
| DTE-DTE¹ | 100m | n/a | 412m/2,000m4 |
| 1 Class-I Repeater³ | 200m | 261m | 272m |
| 1 Class-II Repeater | 200m | 309m | 318m |
| 2 Class-II Repeaters | 205m | 216m | 228m |
| NOTES: 1) "DTE" is an end-station such as a PC or switch port 2) Copper+Fiber assumes the max. Copper length is used 3) "Repeater" is a standard hub, NOT a switching hub. 4) Half-/Full-Duplex. Fiber's distance depends on mode. |

Table D: 100Base-TX/FX Topology Rules

## Auto-Negotiation

The 100Base-TX ports on the FNSW-800 have built-in "Auto-Negotiation". This technology automatically sets the best possible bandwidth when a connection is established with another network device (usually at Power On or Reset). This is done by detect the mode and speed at the second device is capable of. The 100Base-TX devices can connect with the 100Base-TX port in either Half- or Full-Duplex mode.

| If attached device is: | 100Base-TX port will set to: |
| --- | --- |
| 100Mbps, no auto-negotiation | 100Mbps (100Base-TX, Half-Duplex) |
| 100Mbps, with auto-negotiation | 200Mbps (100Base-TX, Full-Duplex) |
| 10Mbps, no auto-negotiation | 10Mbps (10Base-T, Half-Duplex) |
| 10Mbps, with auto-negotiation | 20Mbps (10Base-T, Full-Duplex) |

## MAC Address Table

This 6-byte ID is called the MAC (Media Access Control) Address. Every Ethernet data packet includes both source and destination addresses.

These NOVASwitch models FNSW-800 can automatically learn and store up to 12000 MAC addresses. The MAC address table is volatile: it disappears when the switch is powered off or reset.

Note: When the network needs reconfiguration, we recommend turning off the power first. After all nodes have been moved, power on the switch to rebuild the internal MAC address table. Push the "Reset" button will also force the switch to rebuild the MAC address table.

## Sample Application

The optimal application for the NOVASwitch FNSW-800 or FNSW-800 with the extension module is as a "big pipe" backbone interconnecting file servers with bandwidth-hungry workgroups, departments, and offices.

In the figure, the Port #3 links to another hub‘s Uplink (MDI-II) port, Port #-7-8 connect to 100Mbps Workstations, and Port #1-2 are attached to file servers at 200Mbps. This example highlight the extra distance provided by 100Base-FX fiber-optic, using the Port #8 of FNSW-800 with the rear module installed.

Figure 3: Sample Application for FNSW-800 Models

# Troubleshooting

| Symptom | Link LED does not lit after cable is connected to the port.. |
| --- | --- |
| Checkpoint | Verify that the other end of the cable is connected to a device that is powered on and on-line.. For UTP cable connection to another hub, verify that only one end of the cable is connected to a “Crossover” port. |

| Symptom | 100Base-TX port Link LED is lit, Collision LED is blinking, but traffic is irregular. |
| --- | --- |
| Checkpoint | Check that the attached device is not set to dedicated full-duplex. (Some devices use a physical or software switch to change duplex modes. Auto-negotiation may not recognize this type of full-duplex setting. |

| Symptom | After setting the DIP-switch of the 100Base-FX module, the attached device doesn’t communicate normally with the port. |
| --- | --- |
| Checkpoint | The attached network device MUST be set to operate in the same duplex mode. |

ALWAYS CHECK THAT THE CABLE, LINK DISTANCES, AND OVERALL NETWORK DIAMETER ARE WITHIN SPEC. FOR THE NETWORK TYPE.

# PRODUCT SPECIFICATIONS

| Product | FNSW-800 |
| --- | --- |
| Network Ports | 8 x 10/100Base-TX RJ-45 (MDI-X) |
| Buffer Memory | 4 M Byte |
| Extension Slot | Rear Extension slot shared with port 8 for optional module |
| Media Support | 100Base-TX Cat. 5 UTP, RJ-45 10Base-T Cat. 3, 4, 5 UTP RJ-45 |
| Bandwidth | 100Base-TX, 200/100/20/10Mbps, Auto-Negotiation |
| Filter/ Forward Rate | 148,800 packets/second per port @ 100Mbps, max. 14,880 packets/second per port @ 10Mbps, max. |
| MAC Addresses | Up to 12,000 6-Byte full MAC address entries max. self-learning |
| Switches | 1 for Power On/Off |
| LEDs | 1 for Power On/Off 8 per port for 10Mbps, 100Mbps, Full-Duplex, Half-Duplex, Transmit, Receive, Link, Collision, |
| Power Supply | Auto-switching. Input voltage: 90~250 VAC, 50 ~ 60Hz |
| Environment | Operating Temp: 0 ~ 50(C (32 ~ 122(F) Storage Temp: -30 ~ 70(C (-22 ~ 158(F) Humidity 0 ~ 90% non-condensing |
| Dimensions | 430 x 180 x 44 mm (16.9 x 7.1 x 1.73 in.) |
| Emission | FCC Class A, CE |
| Safety | UL, TUV/GS (EN60950) |

Table E: FNSW-800 Product Specifications

# RJ-45 Pin AssignmeT

| Pin | Hub's Station Ports 1-8 (MDI-X port) | Uplink Port (MDI-II port) |
| --- | --- | --- |
| 1 | Input Receive Data + | Output Transmit Data+ |
| 2 | Input Receive Data - | Output Transmit Data- |
| 3 | Output Transmit Data+ | Input Receive Data + |
| 6 | Output Transmit Data- | Input Receive Data - |
| 4,5,7,8 | Not used | Not used |

Schematics for both straight and crossover twisted-pair cable are shown below. (Note that crossover cable is only required if you cascade hubs via the RJ-45 station ports; i.e. the Uplink port is not used.)

## Straight-Through/Crossover Cable

The pin assignment of the cables both ends should be as below:

| Straight-through | Crossover |
| --- | --- |
| Hub (MDI-X) | Adapter(MDI-II) | Hub (MDI-X) | Hub (MDI-X) |
| Pin 1 | Pin 1 | Pin 1 | Pin 3 |
| Pin 2 | Pin 2 | Pin 2 | Pin 6 |
| Pin 3 | Pin 3 | Pin 3 | Pin 1 |
| Pin 6 | Pin 6 | Pin 6 | Pin 2 |

# Text boxes

EMFNSW800