Series Receiver

Operation Instructions

Please read this manual carefully before use this product

Table of contents

| 1. | Product Description --------------------------------------------- | 3 |
| --- | --- | --- |
| 2. | Features------------------------------------------------------------ | 3 |
| 3. | Specification------------------------------------------------------ | 3 |
| 4. | Pan/Tilt setting---------------------------------------------------- | 4 |
| 5. | Lens setting ------------------------------------------------------- | 4 |
| 6. | Auxiliary control ------------------------------------------------- | 4 |
| 7. | Protocol setting--------------------------------------------------- | 5 |
| 8. | Baud rate setting-------------------------------------------------- | 6 |
| 9. | ID Address setting------------------------------------------------ | 6 |
| 10. | System connections---------------------------------------------- | 7 |
| 11. | Connections and setup------------------------------------------- | 8 |
| 12. | Test function ------------------------------------------------------ | 9 |
| 13. | Trouble Shooting------------------------------------------------- | 11 |
| 14. | Appendix I- Iris control settings for KODICOM RX &KRE-301RX protocol----------------------------------------- | 11 |
| 15. | Appendix II-ID address setting for KODICOM-------------- | 12 |

Warning:

Please choose the Pan/Tilt voltage correctly!

The voltage is too high will lead to the fact that the Pan/Tilt damaged.

Please use twisted-pair cable for wiring.

1、Product Description

The series receivers are used with keyboard controller and matrix systems to control pan, tilt, zoom, focus, and iris and auxiliary functions in surveillance system. Receivers are RS485 or Manchester communication, it is compatible with multi-protocol.

2、Features

- Built in watch dog function, multi-protocol setting

- Two auxiliary relays for light, wiper or camera power controlling

- Fully optical isolation, auto reset function in strong reference environment

- Baud rate options, 0-64-256 ID setting

- Static resistant, high voltage and thunder proof design

- Optional power supply for camera: AC24V, DC12,AC220V(special product)

- AC220V, AC24V voltage optional for pan/tilt unit (the factory default setting is AC24V)

- Adjustable lens voltage form 6V to 12V for speed adjusting (the factory default setting is 8V)

3、Technical parameter

Power supply：AC220V / 50HZ

Power consumption:28－50W

Pan/Tilt voltage：AC220V, AC 24V optional

Pan/Tilt drive power consumption：AC220V／2A or AC24V／800mA

lens voltage：5－12V options

Provided power source：AC220V/2A、AC24V／500mA、DC12V／600mA

Auxiliary relay:2 NO auxiliary(AUX1 and AUX2),the capacity is AC220V／3A

Communication：RS485, Manchester

Protocol: multi-protocol setting (we welcome your request for protocol customization)

Operating environment: indoor(－10℃~70℃),outdoor(－40℃~70℃)

Transmission distance:1200-1500meters

ID setting:0－63－255(Can be customized)

4、Pan/tilt setting

The receiver can control Pan/tilt up, down, left, right movements and auto function. There are two kinds of voltage optional, AC220V&AC24V (warning: higher voltage will lead to the fact that Pan/Tilt be damaged).

5、Lens setting

The receiver can control the iris、focus and zoom of lens. The lens output voltage can be varied from 6 to 12 volts DC with a potentiometer. The operator can adjust the speed of lens via lens power, the voltage is higher then the speed is faster.

6、Auxiliary control

There are 2 auxiliary relay normally open (AUX1&AUX2).

7、Protocol setting

| NO. | Protocol | switch position | Baud rate |
| --- | --- | --- | --- |
| 0 | PELCO-D |  |  | 2400 |
| 1 | HY |  |  | 9600 |
| 2 | VICON (surveyor 99) |  |  | 4800 |
| 3 | KALATEL(KDT-312) DCW0601 |  |  | 9600 |
| 4 | PELCO-P |  |  | 9600 |
| 5 | HN-C |  |  | 9600 |
| 6 | SAMSUNG |  |  | 9600 |
| 7 | KODICOM–RX KRE-301RX |  |  | 9600 |
| 8 | DH/KCL |  |  | 9600/19200 |
| 9 | NEOCAM |  |  | 9600 |
| 10 | PIH1016 (lilin) |  |  | 2400 |
| 11 | B01 |  |  | 9600 |
| 12 | RM110／S1601 |  |  | 9600 |
| 13 | PEARMAIN |  |  | 9600 |
| 14 | V1200 |  |  | 9600 |
| 15 | SANTACHI-450/9600 KALATEL KDT348 |  |  | 9600/ 4800 |

Note: The DV7XX series receiver provides IRIS control for KODICOM&PIACSO

Protocol l, please refer to appendix I for detail setting.

8、Baud rate setting

9、ID Address Setting                 0=OFF      1=ON

| Camera | Switch Position |
| --- | --- |
| ID | 3 | 4 | 5 | 6 | 7 | 8 |
| 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 2 | 0 | 0 | 0 | 0 | 0 | 1 |
| 3 | 0 | 0 | 0 | 0 | 1 | 0 |
| 4 | 0 | 0 | 0 | 0 | 1 | 1 |
| 5 | 0 | 0 | 0 | 1 | 0 | 0 |
| 6 | 0 | 0 | 0 | 1 | 0 | 1 |
| 7 | 0 | 0 | 0 | 1 | 1 | 0 |
| 8 | 0 | 0 | 0 | 1 | 1 | 1 |
| 9 | 0 | 0 | 1 | 0 | 0 | 0 |
| 10 | 0 | 0 | 1 | 0 | 0 | 1 |
| 11 | 0 | 0 | 1 | 0 | 1 | 0 |
| 12 | 0 | 0 | 1 | 0 | 1 | 1 |
| 13 | 0 | 0 | 1 | 1 | 0 | 0 |
| 14 | 0 | 0 | 1 | 1 | 0 | 1 |

| 15 | 0 | 0 | 1 | 1 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| 16 | 0 | 0 | 1 | 1 | 1 | 1 |
| 17 | 0 | 1 | 0 | 0 | 0 | 0 |
| 18 | 0 | 1 | 0 | 0 | 0 | 1 |
| …… |  |  |  |  |  |  |
| 62 | 1 | 1 | 1 | 1 | 1 | 0 |
| 63 | 1 | 1 | 1 | 1 | 1 | 1 |

NOTE:Please give clear indication if order the receiver more than 64 address.

Some of control host ID start from 0, and some of start from 1.

10、System connections

Instruction:

- Please use shielded Twisted Paired for correct connection per RS485 communication standard, otherwise the communication distance will be shorten significantly if using parallel cable.

- The receiver is designed for “star” and “daisy chain” connection, the terminals marked A and B are RS485 signal output ports which is to connect RS485 devices, connection is not allowed.

- When a lot of receivers need to connect together, a 120-ohm resistor must be connected in parallel between the terminal marked A and B on the last piece of equipment on the line.

11、Connections

Economy Type Receiver Connection Diagram

12、The test function instruction

The receiver test function is to test whether the pan/tilt and lens function is available. There are 2 test function keys (K1&K2) on the main PCB. Please refer to the following table1 for DIP switch setting..

Table1, DIP switch setting (ON=1, OFF=0)

Test procedure:

- Short circuit K1 to enter the testing mode, then the red LED blinks.

- Set the DIP switch to the related pan/tilt and lens function, then short circuit the K2 or press the K2 to conduct the test.

- If the function is available the red LED stays illuminated.

- After testing, remove the short wires and restore the DIP switch to the original setting. The receiver back to normal working status.

13、Trouble shooting

| Trouble | Analysis and solution |
| --- | --- |
| LED does not illuminate after powered up | 1、Check the power supply to see if it is connected, or confirm if it is AC 220 volts. 2、 Check to see if the fuse is damaged. 3、 Check to see if the power supply has been cut off. |
| The pan/tilt & lens are uncontrollable | The control cables are connected wrongly or the connection is not good in contact. Check to see if the camera DIP switch setting is correct. Check to see if the communication distance over1200 meters, add a RS485 repeater or equivalent to extend. |

14、Appendix Iris control settings for KODICOM RX & KRE-301RX Protocol

Since the PICASO &KODICOM digital video recorder software has no iris control function, the DV7xx series receiver provides the detail iris control setting.

Operation procedures:

- For KODICOM digital video recorder

- Select KRE-301RX protocol

- Switch the wiper on

- Use focus button to conduct iris control

- Switch the wiper off

- For PICASO digital video recorder

- Select KODICOM RX protocol

- The operation procedure as same as above KODICOM DVR

15、Appendix II-ID address setting for KODICOM

| ID | Switch Position |
| --- | --- |
|  | 3 | 4 | 5 | 6 | 7 | 8 |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 1 | 0 | 0 | 0 | 0 | 0 | 1 |
| 2 | 0 | 0 | 0 | 0 | 1 | 0 |
| 3 | 0 | 0 | 0 | 0 | 1 | 1 |
| 4 | 0 | 0 | 0 | 1 | 0 | 0 |
| 5 | 0 | 0 | 0 | 1 | 0 | 1 |
| 6 | 0 | 0 | 0 | 1 | 1 | 0 |
| 7 | 0 | 0 | 0 | 1 | 1 | 1 |
| 8 | 0 | 0 | 1 | 0 | 0 | 0 |
| 9 | 0 | 0 | 1 | 0 | 0 | 1 |
| 10 | 0 | 1 | 0 | 0 | 0 | 0 |
| 11 | 0 | 1 | 0 | 0 | 0 | 1 |
| 12 | 0 | 1 | 0 | 0 | 1 | 0 |
| 13 | 0 | 1 | 0 | 0 | 1 | 1 |
| 14 | 0 | 1 | 0 | 1 | 0 | 0 |
| 15 | 0 | 1 | 0 | 1 | 0 | 1 |
| 16 | 0 | 1 | 0 | 1 | 1 | 0 |

# Text boxes

| NO. | Baud rate | Switch Position | NOTE |
| --- | --- | --- | --- |
| 0 | 1200／19200 |  |  | According to different protocol, it can select the correct one automatically |
| 1 | 2400 |  |  |  |
| 2 | 4800 |  |  |  |
| 3 | 9600 |  |  |  |

| NO. | Function | Switch Position |
| --- | --- | --- |
|  |  | 5 | 6 | 7 | 8 |
| 0 | Pan Up | 0 | 0 | 0 | 0 |
| 1 | Pan Down | 0 | 0 | 0 | 1 |
| 2 | Tilt Left | 0 | 0 | 1 | 0 |
| 3 | Tilt Right | 0 | 0 | 1 | 1 |
| 4 | Zoom In | 0 | 1 | 0 | 0 |
| 5 | Zoom Out | 0 | 1 | 0 | 1 |
| 6 | Focus Near | 0 | 1 | 1 | 0 |
| 7 | Focus Far | 0 | 1 | 1 | 1 |
| 8 | Iris＋ | 1 | 0 | 0 | 0 |
| 9 | Iris－ | 1 | 0 | 0 | 1 |
| A | AUX1 | 1 | 0 | 1 | 0 |
| B | AUX2 | 1 | 0 | 1 | 1 |