CHAPTER 4

TROUBLESHOOTING

SYMPTOM: The power LED is not lit.

SOLUTION:

If the power LED is not lit after the power adapter is plugged into the concentrator and the power outlet, there may be a power fault.

1. First verify if there is power at the power outlet by plugging in a device which is known to operate.

2. If there is no problem, try to use another power adapter available to verify the status of the original power adapter.

3. If a volt meter is available, measure the voltage on the nylon connector which is plugged into the concentrator.

4. If a volt meter is not available and the second power adapter does not fix the problem, contact the authorized dealer from whom you purchased your concentrator for assistance.

SYMPTOM:  The Link LED is not lit.

SOLUTION:

The Link LED is not on after a workstation is connected to the UTP port of the concentrator.

1. Verify if the workstation and the concentrator are powered up.

2. Verify if the network cable has been attached to the workstation.

3. Verify if the network cable from the Hub to workstation is straight-through and is not crossovered.

4. Verify if the wires to the phone jack pins are connected correctly and the connections are not faulty.

SYMPTOM: When port auto-partitioned out.

SOLUTION:

1. Use another Ethernet adapter to verify if the original Ethernet adapter malfunctions.

2. Connect the twisted-pair cable to another concentrator to verify if the twisted-pair cable can work well.