Trademarks

Copyright ( PLANET Technology Corp.

Contents subject to revision without prior notice.

PLANET is a registered trademark of PLANET Technology Corp. All other trademarks belong to their respective owners.

FCC Warning

This equipment has been tested and found to comply with the limits for a Class B digital device pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference when the equipment is operated in a commercial environment.

This equipment generates, uses, and can radiate radio frequency energy, and if not installed and used in accordance with the instruction manual may cause harmful interference to radio communications. Its operation in a residential area is likely to cause harmful interference in which case the user will be required to correct the interference as his own expense.

Changes or modifications not expressly approved by the parties responsible for compliance could void the user's authority to operate the equipment.

CE Marking Warning

This is a Class A product. In a domestic environment this product may cause radio interference in which case the user may be required to take adequate measures.

Revision:

User's Manual for PLANET PC Card family,

Model: ENW-3502-T

Ethernet PC Card with TP jack only

Part No.: EM3502T

Rev: 1.0 (May, 1999)

About This Manual

This is a user's guide for the ENW-3502-T Ethernet PC Card. Please read this manual before you attempt to install the product.

This manual includes the following topics:

- Product descriptions, features and specifications.

- Hardware installation procedures

- Software installation procedures

### Table of Contents

Table of Contents	ii

Introduction	1

1.1 Product Description	1

1.2 Features	2

1.3 Quick installation	2

Hardware Installation	3

2.1 Package Contents	3

2.2 Hardware Description	3

2.3 Installing the ENW-3502-T Ethernet PC Card	3

Driver Installation for Windows 95	5

Driver Installation for Windows 98	7

Driver Installation for Windows NT 4.0	10

Client Driver Installation	14

6.1 Driver Installation	14

6.1.1 Driver Installation Program	14

6.1.2 Quick Installation	14

6.2 The INSTALL Program	15

6.2.1 Using the INSTALL Program	15

6.3 Manual Installation	23

6.3.1 Enabler	23

6.4 Client Driver Installation	24

6.4.1 NetWare 3.X / 4.X Client	24

6.4.2 Microsoft Windows for Workgroups 3.11	24

6.4.3 Microsoft Windows NT 3.51	24

6.4.4 Microsoft LAN Manager	25

6.4.5 Artisoft LANtastic Version 6.0	25

6.4.6 Configuration Reference	25

Troubleshooting for Windows Environments	26

A.1 Windows 9X	26

A.2 Windows NT 4.0 and 3.51	26

Error Messages of Enabler Program	27

CARDGO.EXE	27

Specifications	29

This page left blank intentionally!

# Chapter 1

## Introduction

### 1.1 Product Description

Thank you for purchasing the ENW-3502-T Ethernet PC Card. The ENW-3502-T Ethernet PC Card is a network adapter card for notebook computers and complies with the PCMCIA TYPE II standard. An Ethernet adapter cable with male RJ-45 connector two kinds of connections :

- Connect to a Hub directly, or

- Connect to a network cable with male RJ-45 connector

The ENW-3502-T Ethernet PC Card is switchless and software configurable. An enabler program can successfully drive the card. Even without the card and socket service drivers for PCMCIA controller installed, you will still be able to use the card by running the enabler program.

### 1.2 Features

- 5.0 mm Type II credit card size

- Complies with IEEE 802.3 10Base-T.

- Complies with PCMCIA Release 2.1 Spec

- PC Card standard 68-pin 16-bit PCMCIA Interface

- Half-duplex 10Base-T

- 5.0V Power consumption

### 1.3 Quick installation

This section briefly outlines the steps needed to install the ENW-3502-T Ethernet PC Card and its driver software, and how to connect the card to the network.

To install the ENW-3502-T Ethernet PC Card to your notebook computer:

- Connect the Ethernet adapter cable to the card, then insert the card into the PCMCIA slot. (Refer to Chapter 2 for details.)

- Connect the Ethernet adapter cable to the network. (See Chapter 2 2.3 Installing the ENW-3502-T Ethernet PC Card for details.)

- Install the driver software like Windows 95/98, NT or other Network Operation System. (See Chapter 3, Chapter 4, Chapter 5, and Chapter 6 for details.)

# Chapter 2

## Hardware Installation

### 2.1 Package Contents

Please check whether the following items are in your package:

- ENW-3502-T Ethernet PC Card

- Ethernet adapter cable with 15-pin flat connector at one end and female RJ-45 connector at the other end for 10Base-T connectivity.

- Plastic protective adapter case

- Driver Diskette (Device drivers, User’s manual)

### 2.2 Hardware Description

The ENW-3502-T Ethernet PC Card is encased in a stainless compact frame that is easily transportable. It has a 68-pin connector and a 15-pin flat connector for attaching to the Notebook and Ethernet adapter cable respectively.

### 2.3 Installing the ENW-3502-T Ethernet PC Card

Follow the procedure below to install the ENW-3502-T Ethernet PC Card.

1.	Turn off the host computer.

2.	With the card’s 68-pin connector facing the PCMCIA slot, slide the card all the way into the PCMCIA slot. Do not force the connection.

3.	Plug the Ethernet adapter cable to the 15-pin connector on the card.

4.	Connect the Ethernet adapter cable to a network. If there is an Ethernet Hub or RJ-45 phone jack connected to a network and is near by your notebook, you can connect the Ethernet adapter cable to a port on the Hub or to the RJ-45 phone jack with another male-to-male RJ-45 line or connector.

- Turn on the computer.

|  | Note: | Use the Network coupler bundled in the package. Use of other coupler could make the PC card or coupler malfunction. |
| --- | --- | --- |

# Chapter 3

## Driver Installation for Windows 95

Installing the ENW-3502-T Ethernet PC Card is just the same as any normal Windows 95 Plug & Play device. Follow the steps below to install.

1.	Insert the ENW-3502-T Ethernet PC Card into an open PCMCIA slot on your notebook.

2.	After Windows 95 detects the card, the Update Device Driver Wizard window, as shown in Figure 3.1, will appear. Insert the driver diskette and click Next to continue the installation.

Figure 3.1 Update Device Driver Wizard

3.	When Windows 95 finds the installation file in Driver Diskette and shows the window in Figure 3.2 on your screen, click Finish.

Figure 3.2 Found Driver

- Windows 95 will follow the direction of the installation file to locate the files that should be copied. Eventually Windows 95 may need to copy required system files. Give the correct path, then click OK to continue.

- After all files have been copied, Windows 95 will prompt you to restart the system. Click Yes to complete installation.

# Chapter 4

## Driver Installation for Windows 98

Installing the ENW-3502-T Ethernet PC Card is similar as any normal Windows 95 Plug & Play device. Follow the steps below to install.

1.	Insert the ENW-3502-T Ethernet PC Card into an open PCMCIA slot on your notebook.

2.	After Windows 98 detects the ENW-3502-T Ethernet PC Card, the Add New Hardware Wizard window, as shown in Figure 4.1, will appear. Click Next to continue the installation.

Figure 4.1 Add New Hardware Wizard

3.	Select Search for the best driver for your device. [Recommended] and click Next.

Figure 4.2 Search Driver

4.	Uncheck the Microsoft Windows Update. Let Windows 98 search floppy- drive only. Then place the floppy driver disk and click Next to continue.

Figure 4.3 Search Floppy Disk drive

- Select the found updated driver, ENW-3502-T Ethernet PC Card, then click Next.

Figure 4.4 The updated driver

- After copying all required files, Windows 98 will prompt you to restart the system. Click Yes to complete installation.

# Chapter 5

## Driver Installation for Windows NT 4.0

The installation procedure assumes the network component has been installed on your computer. To check whether the network component has been installed, double click the Network icon in Control Panel. If it has not, refer to the Windows NT 4.0 installation guide to install the component.

While installing the network component, Windows NT 4.0 will ask you to install the driver of network adapter. The driver installation procedure is similar to the following one.

Follow the steps below to install the driver.

1.	Insert the ENW-3502-T Ethernet PC Card into an open PCMCIA slot on your notebook. Login to NT 4.0 as the administrator.

- Doublic click Network icon in Control Panel, and select Adapters tab, the Figure 5.1 displayed.

Figure 5.1 Network Window

3.	Click Add to add a new adapter, the window, Figure 5.2, popped up.

Figure 5.2 Select Network Adapter Window

4.	Click Have Disk …, after Insert Disk window, shown in Figure 5.3, popped up, give the search path, A:\WINNT (suppose A: is your floppy drive), then insert driver diskette, and click OK.

Figure 5.3 Insert Compact Disk Window

- After finding the installation file, the Select OEM Option window shown in Figure 5.4 is displayed. Click OK to choose the ENW-3502-T Ethernet PC Card option.

Figure 5.4 Select OEM Option Window

- In the ENW-3502-T Ethernet PC Card setup window, Figure 5.5, select the desired IRQ level and I/O Port address. After selecting desired configuration, click OK to continue.

Figure 5.5 Setup Window-1

Select the PCMCIA type option as figure 5.6 and click OK to continue.

Figure 5.6 Setup Window-2

Click Close to close the Network window, and let Windows NT 4.0 binding the adapter with network component.

Eventually, Windows NT 4.0 will prompt you to restart the computer, click "Yes" to finish installation.

# Chapter 6

## Client Driver Installation

### 6.1 Driver Installation

Before your computer system can recognize your ENW-3502-T Ethernet PC Card, the driver programs must first be installed to enable the card.

#### 6.1.1 Driver Installation Program

INSTALL.EXE is the ENW-3502-T Ethernet PC Card driver installation program. The INSTALL.EXE program allows you to do auto-configuration where the program automatically selects the most suitable option settings, or do a custom configuration where you individually select each option setting.

#### 6.1.2 Quick Installation

This section gives a brief overview of the installation process. (For a clearer step-by-step procedure, refer to the next section.)

1.	If the Card and Socket Services software is included as part of your computer, it is recommended that you use this software when installing your ENW-3502-T Ethernet PC Card.

A system with Card and Socket Services installed allows the PCMCIA card to automatically configure itself. While the system is on, available system resources and insertion or removal of the card will automatically be detected.

2.	Run the INSTALL.EXE program found on your Installation floppy disk. The install program guides you through the installation process and will install the network drivers needed to run the card on your network operating system.

If you have successfully completed the installation, jump to step 5. If installation was unsuccessful, then go on to next step.

3.	Use the Card Service client driver, CARDGO.EXE, found on your Installation floppy disk. You can install the client driver by typing CARDGO at the DOS prompt or including it as a line in your CONFIG.SYS or AUTOEXEC.BAT file. When installing the client driver, it is important to note that the driver should be loaded after Card and Socket Services are loaded.

4.	Turn off your computer and insert the ENW-3502-T Ethernet PC Card into the PCMCIA socket. The card is keyed to go in one way only. Then attach the network cable to the card.

5.	Now turn your computer on and connect to your network. If you cannot connect to the network, refer to the Appendix B and C.

### 6.2 The INSTALL Program

Before you can use your ENW-3502-T Ethernet PC Card, you need to install and modify some files in your computer system. You can make these changes manually, or you can let the INSTALL.EXE program do them for you.

This section explains how you can use the INSTALL.EXE program to install the enabler and the files needed by the network operating system.

#### 6.2.1 Using the INSTALL Program

To run the INSTALL.EXE program, type INSTALL and press <Enter> at the DOS prompt. You should see an opening screen that welcomes you to the program and asks if you wish to continue.

Figure 6-2.1 Opening Screen

Press <Enter> to continue the installation.

The program will then prompt you for the directory where you want to install the driver files. You can choose the default directory name or enter a new name. Then, press <Enter> to continue with installation.

Figure 6-2.2 Specify Directory Path

The next screen asks if you want to do an Auto Configuration or a Custom Configuration. Select Auto Configuration if you want to do a quick installation and use the default configuration settings. If you wish to individually set any of the settings, then select Custom Configuration.

Figure 6-2.3 Select Auto or Custom Installation

6.2.1.1 Auto Configuration

If you selected Auto Configuration, the program will auto detect which IRQ, I/O Port and Memory addresses the ENW-3502-T Ethernet PC Card can use. After auto-detecting the configuration successfully, the program will show the following screen:

Figure 6-2.4 Configuration Information

After the configuration process, you will be prompted to select the type of network that you are installing the drivers into. Select a Network Operating System from the list by moving the cursor to your selection and pressing <Enter>.

Figure 6-2.5 Network OS Selection

After selecting the Network Operating System, the INSTALL program will copy and/or modify some files on your boot drive. Your CONFIG.SYS file will also be modified to include the Client Driver. You should see the following message if installation has been successful.

Figure 6-2.6 Successful Installation Screen

6.2.1.2 Custom Configuration

To do a custom installation, you need to select the Custom Configuration Menu after you begin the INSTALL program.

After selecting the Custom Installation Menu, you will see a series of submenus prompting you to select an IRQ, I/O port and Memory address.

Interrupt Select

The first submenu, which will appear, is the Interrupt submenu. To select an interrupt, move the cursor to the interrupt of your choice and select it by pressing <Enter>. Interrupts available for your 10Mbps Ethernet card include 2, 3, 4, 5, 6, 10, 11, 12 and 15.

Figure 6-2.7 Select Interrupt

IO Port Select

To select an I/O Port, move the cursor to your selected I/O address and press <Enter> to select. Available I/O Ports are 240H, 280H, 300H, 320H, 340H and 360H.

Figure 6-2.8 Select I/O Port

Memory Address Select

To select a memory address, move the cursor to your selected memory address and press <Enter> to select. Available I/O Ports are D000H, D400H, D800H and DC00H.

Figure 6-2.9 Select Memory Address

### 6.3 Manual Installation

In most cases, the INSTALL program can make all system changes necessary for using your ENW-3502-T Ethernet PC Card. But in some cases, you may wish to make the change manually. This section explains the driver and file modifications needed to enable your ENW-3502-T Ethernet PC Card.

#### 6.3.1 Enabler

A Card Service client driver, CARDGO.EXE, can enable the ENW-3502-T Ethernet PC Card.

CARDGO.EXE

The Card Service client driver, CARDGO.EXE, communicates with the PCMCIA controller of your computer. This program is needed only for DOS and Windows 3.1 systems. The INSTALL program will automatically add a line to your CONFIG.SYS file using the following syntax and format:

DEVICE = [path_name] CARDGO.EXE [/INT=x] [/PORT=xxx] [/mem=xxxx] [/?]

Where:

| [/INT=x] | Specifies the hardware interrupt (IRQ) where your card will be indicated. Default value is 5. The valid IRQs are 3,4,5,6,9,10,11,12,15. |
| --- | --- |
| [/PORT=xxx] | Specifies the I/O port. Default value is auto detect. The valid port addresses are 240H, 280H, 300H, 320H, 340 and 360H. [/MEM=xxxx] Specifies the Memory address. Default value is auto detect. The valid addresses are D000H, D400H, D800H and DC00H. |
| [/?] | Displays all possible command syntax. |

You can also run the CARDGO.EXE by typing “CARDGO” at the DOS prompt or by including it as a line in your AUTOEXEC.BAT file.

After you executed CARDGO.EXE, you will see the following display indicating that installation was successful:

Socket	: 0	(for example)

IRQ Number	: 05	(for example)

I/O PORT Base	: 0300H

Memory Address	: D400H	(for example)

Node ID	: 00 A0 0C 01 00 3A	(for example)

The list of error messages the client driver may display and the correction methods we suggest are given in Appendix B.

### 6.4 Client Driver Installation

#### 6.4.1 NetWare 3.X / 4.X Client

Installation procedure:

- Execute INSTALL program, and choose NetWare ODI Driver.

- Follow the prompts to compete the installation.

- Reboot the computer.

- Log in to the network.

#### 6.4.2 Microsoft Windows for Workgroups 3.11

Installation procedure:

- Execute install.exe, and choose Windows for Workgroups.

- Run Windows by typing WIN from the DOS prompt.

- Click the "Network" icon in the Main Program Group.

- Click the "Network Setup" icon from the Network window.

- Select "Drivers" item from the Network Setup dialog box.

- Select "Add Adapters" item in the Option dialog box.

- Select "Unlisted or Updated Network Adapter" when the Install driver field appears.

- Type the path, A:\wfw311 (where A: is the floppy drive), and press <Enter>.

- When the "ENW-3502-T Ethernet PC Card" dialog box appear, select the options step by step.

- Follow screen instructions to complete the process.

- Restart your computer.

#### 6.4.3 Microsoft Windows NT 3.51

Installation procedure:

- Insert ENW-3502-T Ethernet PC Card into an open PCMCIA slot.

- Boot the computer.

- Click Control panel in the main window, then click Network icon.

- Click Add Adapter. Then pull down the adapter’s list and select <other>. Requires disk from manufacturer, then click continue.

- Type A:\winnt (where A: is your floppy drive), then click OK.

- Set the proper IRQ and IO Port settings for this card.

- Set bus type to be PCMCIA and bus number to be 0.

- Reboot the computer and installation is completed.

#### 6.4.4 Microsoft LAN Manager

Installation procedure:

1. Run INSTALL program, and choose LAN Manager.

2. Type "lmsetup" In LAN Manager Directory. Press Enter

3. Choose "Network Drivers" in "Configuration". Press Enter.

4. Choose <Add New Configs> ,press Enter.

5. Choose <Other Driver> , press Enter.

6. Insert the Driver Diskette, and specified drive A:\  (where A: is the floppy drive), then push <OK> button.

7. Select the Network Adapter Driver, "ENW-3502-T Ethernet PC Card", then push <OK> button.

8. Press the SPACEBAR to select the protocol that you want.

9. Push <OK> button. Configuration Complete appear.

10. Push <Save> button, then press "F3" to exit.

#### 6.4.5 Artisoft LANtastic Version 6.0

Installation procedure:

1. Run INSTALL program, and choose LANtastic.

2. Install the Artisoft LANtastic, and specify C:\LANTASTI as the destination directory.

3. When “Select network adapter” screen popped up, choose “NDIS Support for Network Adapters”.

4. When install program prompts you the “manufacturer’s driver disk” on the “Enter NDIS driver directory” screen, insert the driver diskette.

5. Complete the installation, then reboot the computer and start LANtastic.

#### 6.4.6 Configuration Reference

The configuration reference of each NOS client driver can be found in the readme.txt file of the associated subdirectory of the driver diskette.

# Appendix A

## Troubleshooting for Windows Environments

These guidelines give you tips to deal with some problems on using ENW-3502-T Ethernet PC Card. If the problems remain unsolved, contact your dealer for assistance.

### A.1 Windows 9X

1.	Ejecting the card from the PCMCIA socket hangs or reboots the computer.

Solution: To prevent this phenomenon from occurring, stop the card by using the PC Card tool in the Control Panel or the PC Card icon on the taskbar before you remove the card.

2.	The card can not be detected when reinserted

It is caused by certain unstable PCMCIA status lines for a time when the card is removed and reinserted. The Windows 9X drivers may read an incorrect status during this period of signal instability, and fail to detect the correct status of the card.

Solution: The card can be detected by clicking “Refresh” in Device Manager.

### A.2 Windows NT 4.0 and 3.51

Does the driver support “hot-swap” on NT 4.0 and 3.51?

Answer: Windows NT 4.0 and 3.51 are not plug-and-play systems. If you want to remove the card, shut down the computer and remove it.

# Appendix B

## Error Messages of Enabler Program

### CARDGO.EXE

Here is the list of error messages the CARDGO.EXE may display and correction method we suggested.

[Error 1]	"ENW-3502-T Ethernet PC Card enabler failed in request IRQ."

The IRQ number you specified is not supported by the Card Services or is in conflict with another device.

Correction:	Change the IRQ number to a valid setting, as listed above.

[Error 2]	"ENW-3502-T Ethernet PC Card enabler failed in request I/O port."

The IO port you specified is not supported by the Card Services or is in conflict with another device.

Correction:	Change the IO port to a valid setting, as listed above.

[Error 3]	"ENW-3502-T Ethernet PC Card enabler failed in request memory window."

The memory address you specified is not supported by the Card Services or is in conflict with another device.

Correction:	Change the memory address to a valid setting, as listed above.

[Error 4]	"General error."

Register service failed with Card Services program.

Correction:	Reboot the system and try again.

[Error 5]	"Your Card Service is not compliant with Version 2.00 or higher!"

Correction:	Re-install a new version of Card Service.

[Error 6]	"ENW-3502-T Ethernet PC Card is not active ! Enable again."

Maybe the Ethernet controller malfunctioned.

Correction:	Enable again. If it still can not work, contact your dealer.

[Error 7]	"Your Card Services is outdated."

"Please install new version of Card Service."

Correction :	Re-install a new version of the Socket and Card Services program.

[Error 8]	"Parameter too long."

Too many parameters issued with CARDGO.

Correction :	Refer to the default syntax listed above and correct it.

[Error 9]	"Unknown parameters."

CARDGO.EXE Syntax error.

Correction :	Refer to the default syntax listed above and correct it.

[Error 10]  "Invalid value !"

An invalid parameter value was issued.

Correction :	Refer to the valid settings listed above and correct it.

[Error 11]  "Card Service Driver is not loaded."

"Please load the Card & Socket Service Drivers first, or use "CARGGO.EXE" to enable the card directly."

Correction :	As the description of the error message indicates.

[Warning 1]  "ENW-3502-T Ethernet PC Card Client Driver is already resident."

CARDGO.EXE has already been executed.

Correction :	If you want to change the parameter setting, reboot your system.

[Warning 2]  "Please insert ENW-3502-T Ethernet PC Card."

The ENW-3502-T Ethernet PC Card is not detected.

Correction :	Insert the card.

# Appendix C

## Specifications

| Model: | ENW-3502-T |
| --- | --- |
| Standards Conformance: | IEEE802.3 10BASE-T |
| Card Size: | 5.0mm Type II |
| Bus Width: | 16-bit |
| Communication Mode: | Half-duplex |
| Media Supported: | UTP-3,4,5 for 10Base-T |
| Operating Distance: | 100m maximum hub to node distance |
| Network Interface: | RJ-45 connector for 10Base-T |
| Socket Interface: | 68-pin 32-bit PCMCIA socket connector |
| Temperature: | 0C to 60 C (Standard Operating) |
| Certification: | FCC Class B |

# Text boxes

PLANET ENW-3502-T Ethernet PC Card Installation Program

DO YOU WANT TO PROCEED?

Welcome to 10Mbps Ethernet Card Installation Program. INSTALL will set up your 10Mbps Ethernet Card.

If you have your network operating system installed, please insert your Card in any available PCMCIA slot on your computer and press <Enter> to continue.

Otherwise press <F3> to return to DOS.

<Enter> to continue   <F3> to return to DOS

PLANET ENW-3502-T Ethernet PC Card Installation Program

ENTER PATH TO INSTALL

INSTALL will create a directory with all of the necessary files to use 10Mbps Ethernet Card. Please enter the drive and directory name, or confirm default displayed.

C:\PCMCIA

<Enter> to continue   <F3> to return to DOS

SELECT AUTO OR CUSTOM CONFIGURATION

To configure your 10Mbps Ethernet Card, you can select either Auto Configuration or Custom Configuration. Using the Auto Configuration Option, the INSTALL program will automatically configure your 10Mbps Ethernet Card. Select Custom Configuration if the default configuration does not work for you or if you want to specify the Interrupt, I/O address.

ENW-3502-T Ethernet PC Card Installation Program

Auto Configuration

Custom Configuration

<Enter> to continue   <F3> to return to DOS

CONFIGURE ENW-3502-T Ethernet PC Card

INSTALL program has detected the following configuration options for your 10Mbps Ethernet Card.

PLANET ENW-3502-T Ethernet PC Card Installation Program

IRQ		  : 5

IO BASE	  : 0x300

MEMORY ADDRESS: 0xD400

<Enter> to continue   <F3> to return to DOS

SELECT DRIVERS YOU WANT TO INSTALL

Please select the network drivers that you want to install. Use the arrow key to highlight the desired item. When a item is highlighted press <Enter> to select it. If the network drivers that you want to install to is not in the following list, please press <Esc> to continue.

PLANET ENW-3502-T Ethernet PC Card Installation Program

NetWare ODI Driver

Packet Driver

Windows for Workgroups

LAN Manager

Artisoft LANtastic

<Enter> to continue <Esc>to continue <F3> to return to DOS

INSTALLATION SUCCESSFUL !

INSTALL has created/modified your AUTOEXEC.BAT and CONFIG.SYS file to enable the 10Mbps Ethernet Card. The original file has been renamed to AUTOEXEC.PCM and CONFIG.PCM. If you have any problems with the new CONFIG.SYS file when you reboot your computer, you should restore the original files.

Please remove the Driver Installation Disk and reboot your computer.

PLANET ENW-3502-T Ethernet PC Card Installation Program

Press any key to return to DOS

SELECT INTERRUPT

Please select the hardware interrupt that you would like your 10Mbps Ethernet Card to use. Use the arrow key to highlight the desired value. When a value is highlighted press <Enter> to select it.

PLANET ENW-3502-T Ethernet PC Card Installation Program

2

3

4

5

6

10

11

12

15

<Enter> to continue   <F3> to return to DOS

SELECT I/O PORT

Please select the I/O Port that you would like your 10Mbps Ethernet Card to use.

Use the arrow key to highlight the desired value. When a value is highlighted press <Enter> to select it.

PLANET ENW-3502-T Ethernet PC Card Installation Program

240H

280H

300H

320H

340H

360H

<Enter> to continue   <F3> to return to DOS

SELECT Memory Address

Please select the Memory Address that you would like your 10Mbps Ethernet Card to use.

Use the arrow key to highlight the desired value. When a value is highlighted press <Enter> to select it.

PLANET ENW-3502-T Ethernet PC Card Installation Program

D000H

D400H

D800H

DC00H

<Enter> to continue   <F3> to return to DOS