Upgrading the Firmware

The switching hub firmware can be upgraded using TFTP (Trivial File Transfer Protocol).  The TFTP application is found on most TCP/IP packages.  Note that upgrading the switching hub’s firmware is done through a station connected to one of the ports on the switching hub.

The following screen examples are from NetManage Inc.’s “Chameleon” TFTP software.  When the TFTP application is accessed, you should see the following menu screen:

Picture app2-1.jpg here

The following instructions show you how to upgrade the firmware using TFTP.

Picture app2-2.jpg here

Note:  It is necessary to modify the TFTP timeout values for “retransmit” and ”total transmit.“ Refer to the User‘s guide gor your application. The values should be set as follows:

Retransmit = 30 seconds

Total transmit = 120 seconds

Select Transfer from the TFTP menu bar.  You should then see the following menu screen.

Type the IP address of the switching hub in the Ho