POST Diagnostics

When the switching hub is turned on for the first time, it runs a POST diagnostics routine.  The Port LEDs on the front panel would start flashing green in sequence from port 1 to port 12 while the routine is running.  If an error condition occurs, the diagnostic routine would stop and  one of the lower port LEDs (Ports 1 to 12) will blink continuously orange.  Red LEDs signify an error condition.  Note that green LEDs signify normal operating conditions while blinking orange LEDs signify an error condition.  If the error condition persists then one LED on ports 1 to 12 will blink orange.  If this happens, one of the components on the switching hub might be defective - you will have to return the switching hub to your dealer to have it repaired.

Note:  Normally, when an error condition is detected, the POST will stop and an LED will blink continuously.  If an EEPROM fails an LED will blink five times before continuing with the rest of the POST.

The following table lists POST error details.

| FHSW-1202 Port | FHSW-1212 Port | Error Condition |
| --- | --- | --- |
| P1 | 1 | Fail EPROM test |
| 1 | 2 | Fail SRAM Read/Write test |
| 2 | 3 | Fail Management Board ID test |
| 3 | 4 | Fail SCC8530 test |
| 4 | 5 | Fail EEPROM checksum, Read/Write test |
| 5 | 6 | Fail NIC RTL8091 test |
| P2 | 7 | Fail I/O board (low) ID test |
| 6 | 8 | Fail I/O board (high) ID test |
| 7 | 9 | Fail NuCleus NC16880 test |
| 8 | 10 | Fail Flash memory test |
| 9 | 11 | Fail Jump to Flash Code & Operation test |

Table C-1POST Error Details