Technical Specifications

FHSW-1202 Switching Hub

Port Configuration

Two (2) 100Base-TX switching ports & Ten (10) 10Base-T ports

Twelve RJ-45 connectors

Learn/Filter/Forward

148,800 pps x 2 per 100Base-TX port

14,880 pps x 2 per 100Base-TX port

4K MAC Address Learning Table per port

Automatic self learning at full wire speed

Parallel store and forward switching

Error filtering

Network management

In-band & out-of-band SNMP network management using PLANET PlanetView or other popular SNMP managers

Port & System Indicators

Rx/Tx, half/full duplex link or disable LEDs per port

Power, DIAG, Virtual LAN, SNMP, Parallel Links & Bandwidth usage LEDs for system

Boot and configuration

S/W downloadable & Configuration stored in NVRAM

Standards supported

IEEE 802.3u 100Base-TX

IEEE 802.1d, MIB-II (RFC 1213), Bridge MIB (RFC 1493)

Dimensions & Weight

356mm x 442mm x 66mm (LxWxH)

6.2 kg

Environment

Operating/Storage temperature: 0 to 50 degree C/ -10 to 65 degree C

Operating humidity: <95% (non-condensing)

Electromagnetic Emissions

FCC Part 15, Subpart B, Class A

EN 55022 (CISPR 22: 1985), Class A

Safety

UL 1950, CSA 950, E