Traps

This section lists the trap definitions used by PLANET’s PlanetView SNMP Network Management System.

| Level | Trap | Description |  | 2 |
| --- | --- | --- | --- | --- |

001

002

336

337

339

340

357

528

529

Become the new root of the Spanning Tree.

Spanning tree topology change.

Accumulated threshold is reached.

Rate threshold is exceeded.

Port accumulated threshold is reached.

Port rate threshold is exceeded.

Primary port has been changed.

NuCleus Error: switch system channel error.

| NuCleus Error: switch port internal error. |  | 3 |
| --- | --- | --- |

256

257

258

259

272

273

288

289

530

624

625

644

645

Successfully reset the switching hub.

Factory reset of the switching hub is successful.

Factory reset switch invoked factory reset.

Successful self-test.

Mount a unit.

Dismounted a unit.

Enable a port.

Disable a port.

NuCleus Error: switch port TX CRC error

Enable Virtual LAN function.

Disable Virtual LAN function.

Operation mode is changed in parallel link function.

| Reconfigure range for parallel link function. |  |
| --- | --- |

Table E-1 Trap Definitions

| Level | Trap | Description |  | 4 |
| --- | --- | --- | --- | --- |

304

305

308

309

320

321

322

544

560

561

592

593

594

608

609

612

613

640

641

Enable intrusion control.

Disable intrusion control.

Enable intrusion control for a port.

Disable intrusion control for a port.

Enable group intrusion control for a master hub.

Enable group intrusion control for a port on a master hub.

Disable group intrusion control for a port on a master hub.

The address tables pack-cou