Getting Started

About Switching Hubs in General

Switching hubs have emerged to become a cost effective solution to congested Ethernet networks.  Ethernet switching hubs are becoming a popular alternative to bridges and routers which are used to segment large Ethernet networks.  The switching hub is a novel and uncomplicated way to segment a congested Ethernet network to increase bandwidth.  Unlike bridges and routers, switching hubs offer a higher level of performance without the higher cost.  There is also the added advantage of maintaining your investment in your existing cabling plant.  You get higher effective bandwidth without the need to lay new cable.

About the FHSW-1202 (10/100 Mbps Switching Hub)

The FHSW-1202 is an intelligent 10/100 Mbps switching hub.  This switching hub has 2 switched 100Base-TX ports capable of 100 Mbps (half-duplex) or 200 Mbps (full duplex) throughput.  In addition there are also 10 switched 10Base-T ports capable of 10 Mbps or 20 Mbps (full duplex) throughput.  The switching architecture of this hub gives you a maximum bandwidth of 600 Mbps per second (full duplex).  The two Fast Ethernet 100Base-TX ports can also be used to set up high speed parallel links to other P

12 switched ports

Fast Ethernet 100Base-TX ports

FHSW-1202 - 2 ports

FHSW-1212 - 12 ports

10Base-T ports

FHSW-1202 - 10 ports

Parallel Link Ports

FHSW-1202 - 2 ports

FHSW-1212 - 4 ports

Parallel Store and Forward architecture

Complete runt and CRC filtering

Full-Duplex system architecture

Flow control (half duplex mode 	      only)

High Speed Parallel Link ports

Configurable for Virtual LANs

Spanning Tree protocol support

SmartAgent support

SNMP over IP protocol

Repeater and Bridge MIB

Broadcast storm control

Easy software upgrades

BootP

TFTP

Local Management

Software upgradeable firmware

Using the 100Base-TX Ports

Fast Ethernet ports give you a 100 Mbps high speed connection.  These ports are best used to connect to devices with high bandwidth requirements such as servers and other hubs.  When connecting to a server, it is necessary that the serverHS-60, FHSW-1212, and other FHSW-1202s, the full duplexed 100Base-TX ports can be used for maxi

Figure 1-2 here

Figure 1-2  FHSW-1

Figure 1-3 here

Figur

Figure 1-4 here

Figure 1-4  FHSW-1212 Front Panel

Parallel Link Ports

Parallel Link ports are specially marked.  On the FHSW-1202, ports P1 and P2 are parallel link ports.  On the FHSW-1212, ports 1, 2, 7, and 8 are the parallel link ports.  These parallel link ports are used to connect to other PLANET intelligent hubs and have a maximum throughput of 200 Mbps per port, full duplexed Fast

LEDs

LEDs on the front panel of the FHSW-1202 and FHSW-1212 display port status as follows:

| LED | Color | Indicates |  | 10Base-T port LEDs Ports 1 to 10 (FHSW-1202) |  | Upper | Green | Link is present |  |  | Flashing green | Port is forwarding packets to another port on the hub. |  |  | Amber | Port is not allowed to receive packets. |  | Lower | Green | Full duplex mode is enabled for the port. |  |  | Flashing green | Port is transmitting packets. |  |  | Amber | Port is not allowed to transmit packets. |  | 100Base TX port LEDs Ports 1 to 12 (FHSW-1212), Ports P1 & P2 (FHSW-1202) |  | Upper | Green | Link is present; port enabled. |  |  | Flashing green | Port is forwarding packets to another port on the hub. |  |  | Amber | Port is not allowed to receive packets. |  | Lower | Green | Full duplex mode is enabled for the port. |  |  | Flashing green | Port is transmitting packets. |  |  | Amber |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Port is not allowed

System Defaults

The following table shows factory defaults for the FHSW-1202/FHSW-1212 switching hubs.

| Function | Default Setting |  | Port Status | Enabled |  | Half Duplex | Enabled |  | Flow Control | Enabled |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Spanning Tree

Bridge priority

Bridge priority

Hello Time

MAX age

Forward Delay

Port level

Port priority

Port path cost (100 Mbps)

(10 Mbps)

32768

2 sec.

20 sec.

15 sec.

128

10

| 100 |  | Password | None |  | Virtual LAN | Disabled |  | Parallel Link | Disabled |  | Port Monitoring | Disabled |  | Filter | Disabled |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Table 1-2 Factory Default

Managing the FHSW-1202 and FHSW-1212

Out-of-band management

The menu driven interface built into the FHSW-1202 and FHSW-1212 switching hubs is known as the VT100 interface.  It can be accessed through the console port at the front of the switching hub.  A connection to the console port is made using a standard serial cable.  A personal computer running terminal emulation software is usually the best way to manage the switching hub through the console port.

In-band management

The FHSW-1202 and FHSW-1212 switching hubs can also be managed through an SNMP manager (such as PLANET’s PlanetView Network Management System or HP’s OpenView Management System for Windows) if the Management Information Base (MIB) is installed correctly in the management station.  The switching hub supports SNMP over IP protocol.  Remote management of the hub through SNMP is possible through a connection using a modem attached to the hub with a null modem cable.

Quick Start for SNMP Users

This section describes how to get started if you wish to use an SNMP manager.  It assumes you are already familiar with SNMP management.

If you need more information about IP, see section 3.2 Managing Over the Network.

If you are using IP and you have a BootP server set