Installation	 and Setup

Selecting a location for the switch

The FHSW-1202 and FHSW-1212 is suitable for use in the office where it can be mounted in a standard 19 inch equipment rack, or left free standing.  Alternatively, the unit can be rack-mounted in a wiring closet or equipment room.  Mounting brackets and screws are included in the package.

When deciding where to locate the switch, make sure that:

You will be able to meet the cable guidelines detailed in the following section.

It is accessible and cables can be connected easily.

Cabling is away from:

Sources of electrical noise such as radios, transmitters, and broadband amplifiers.

Power lines and fluorescent lighting fixtures.

Water or moisture cannot enter the case of the unit.

Air-flow around the unit and through the vents in the side of the case is not restricted.  We recommend that you provide a minimum of 25mm (1 inch) clearance on all sides.

No objects are placed on top of the unit or stack.

Units are not stacked more than four high if free standing.

Cabling Guidelines

Figure 2-1 illustrates the key rules for connecting Fast Ethernet hubs and provides examples of how these rules allow for large scale 100Base-TX networks.

The key 100Base-TX rules are:

Maximum UTP cable length is 100 meters (305 ft.) over category 5 cable.

When connecting two switches, a 100 meter cable run is permitted.  If the distance between the two switches is greater than 100 meters, use of a PLANET  MicroBridge can allow you to extend the distance by an additional 100 meters or up to 2 kilometers using a fiber optic connection.

Figure2-1 here

Figure 2-1  Cable Guidelines

Installing the switching hub

Rack Mounting

The FHSW-1202 and FHSW-1212 switching hubs are 1.5U high and will fit most standard 19 inch racks.  The mounting brackets supplied with the unit should be attached before installing the switching hub to the rack.

Warning:  Disconnect all cables from the switching hub before continuing.  Remove all self adhesive pads from the underside of the unit if already fitted.

Place the unit the right side up on a hard, flat surface with the front facing you.

Locate a mounting bracket over the mounting holes on one side of the unit as shown in Figure 2-2.

Insert the screws and fully tighten with a Phillips screwdriver.

Repeat the two previous steps for the other side of the unit.

Insert the unit into the 19 inch rack and secure with suitable screws (not provided).  EnParalles on the PLANET hubs divide the network traffic into two or more link paths.  This is similar to having two paths to Paralle ports are 100 Mbps, full/half duplex ports.

To use the parallel link option you will need two or more crossover cables.  The FHSW-1202 has two parallel link ports which give a total bandwidth of 400 Mbps, while the FHSW-1212 has four parallel link ports for a total bandwidth of 800 Mbps.  When connecting two FHSW-1202 switching hubs, the two crossover cables are connected to ports P1 and P2 of both hubs.  When connecting two FHSW-1212 hubs, you can use two or four parallel links.  The crossover cables are connected to ports 1, 2, 7, and 8 on the FHSW-1212 hubs.

Figure 2-5 here

Figure 2-5  Single Link Connection

Figure 2-6 here

Figure 2-6  Parallel Link Connection (one pair)

Figure 2-7 here

Figure 2-7  Parallel Link Connection (Two Pairs)

Full Duplex

For an added performance boost, you can enable full duplex operation on the parallel link ports.  For full duplex mode to work, it is necessary that both the connected devices are configured for full duplex mode.  To configure the parallel link ports of the FHSW-1202 and FHSW-1212 switching hubs, it would be necessary to use the console program or an SNMP manager to change the default setting of half duplex.  Note that all other ports on the FHSW-1202 and FHSW-1212 switching hubs can also be configured as full duplex ports.

Connecting to other Ethernet hubs

To connect to other Ethernet hubs you would need to have a crossover cable.  Before making the connection between the two hubs, you have to determine the type of connection you require.  You can connect 100Base-TX 100 Mbps ports or 10Base-T 10 Mbps ports.  On the FHSW-1202, both types of connections are possible. On the FHSW-1212, only 100Base-TX 100 Mbps ports are available for connecting to other Ethernet hubs.  On both the FHSW-1202 and FHSW-1212, all ports ca