Setting Up for Management

Managing the Expr wit hub using one of the following methods:

Access the console program by connecting a terminal (or workstation with terminal emulation software) to the switching hub’s console port.

Use an SNMP network manager over a network connected to the switching hub (in-band managExpre wit hub is known as the Console Program.  The console program is accessed only through a serial connection between the management terminal and the console port of the switching hub.  The management terminal used for the connection may be a VT100 terminal or a PC runni

Managing Over the Network

Any network manager running the SimExpress hub provided the MIB (Management Information Base) is installed correctly on the management station.

Each network manager provides its own user interface for managing SNMP compliant devices.  PLANET’s PlanetView Network Management System or HP OpenView Management System for Windows may also be used to manage the switching hubs.

PLANET’s switching hubs support SNMP over IP protocol.  Note that both PLANET’s PlanetView and HP OpenView can be run using the IP protocol..

IP Addresses

IP (Internet Protocol) addresses have the format n.n.n.n where n is a decimal number between 0 and 255.  An example IP address is: 168.168.8.100

IP addresses are made up of two parts:

The first part (168.168 in the example) identifies the network on which the device resides.  Network addresses are assigned by three organizations.  Depending on your loca

If you later connect to the outside world, you must change all the arbitrary IP address, to comply with those you have been allocated by NIC.  If you do not do this, your outside communications will not operate.

A subnet mask is a filtering system for IP addresses.  If you are unsure about what mask to use, we suggest you use a general mask, 255.255.0.0 to tie in with the advice above.

Navigating the Console Program Screens

The main menu screen shows the different submenus available to your switch.  Before you access the main menu you might see a screen requesting for a password.  If you see a password screen, type in the required password and press the <Enter> key to access the main menu screen.

Submenus on the menu screen are selected by moving the cursor to the desired submenu and pressing the <Enter> key.

Screen Information

The submenu screens would show the following information:

| Type of information | Description |  | Status Field | A Status Field shows the operating status of the selected port. You can only view the contents of this field without being able to change it. |  | Choice Field |
| --- | --- | --- | --- | --- | --- | --- |

A Choice FiExpress hub.  The next few chapters would describe the console program submenus in greater detail.  To use the console program it would be necessary to follow these steps:

Connect a terminal (or a PC with terminal emulation software) to the console port using a serial cable.

Set your terminal to the following settings:

Baud rate - 9600

Parity - None

Character Size - 8

Stop Bit - 1

At the terminal press <Enter> four times to access the console program.  If your settings are correct you should see the