Console Program Essentials

Console program command overview

After gaining access to the on-board console program, you will see the following main menu screen.

Picture 4-1 here

The main menu of the on-board console program consists of the following sub-menus.

System Configuration - This menu allows you to configure the switching hub.  It allows you to name the hub, set IP, Subnet Mask, and Default Gateway addresses, see up time for the hub, set trap level, and enable BootP/RARP.

Set Trap Destination - This menu allows you to type in the IP addresses where SNMP traps are sent.

Set Device Community - This menu allows you to use SNMP community names and to set access modes for these community names.

Statistics Report - This menu lets you see the statistics for each port on the switching hub.

Traffic Generator - This menu is used when testing the switching hub.  You can use this menu to generate traffic to a specific switching port on the hub.

Password Change - This menu allows you to change the password to the console program.  When you use the console program for the first time, there is no password required.  Use this menu if you wish to add a password to control access to the console program.

Warm Start - This menu is used to reset the switching hub.

Factory Reset - This menu resets the switching hub to the factory default settings.  Use this menu when you wish to use the factory default settings.

Switching Port Configuration - This menu is used to configure the     Configure the system

4.2.1  System Configuration menu

When the switching hub is installed for the first time, it would be necessary to configure the system by selecting the 1.  System Configuration menu.  Selecting the menu would give you the following screen:

Picture 4-2 here

The System Configuration menu allows you to configure the following switching hub parameters:

Name:  This parameter allows you to name the device.  You can use up to 31 characters to name your device.  This parameter is used for reference purposes and we advise you use a descriptive name to help identify the purpose of the device in relation to the total network.  For example you may choose to give names such as “Backbone Switch 1” or “Finance Department Switch 1”, etc.

Location:  Like the Device Name parameter, the Location parameter is descriptive and used for reference purposes. For example you may type in location names such as “PLANET, Taipei.

IP Address:  If using IP, a unique IP address must be typed into this field.  IP (Internet Protocol) addresses have the format n.n.n.n where n is a decimal number between 0 and 255.  An example IP address is: 168.168.8.100.

MAC Address:  This is the unique MAC address assigned to the switching hub.  The console program will not allow you to access this field to change the MAC address of your switching hub.

Subnet Mask:  This field allows you to specify the subnet field for the switching hub’s IP address.  The default subnet mask value is 255.255.0.0.  Default subnet values for the three internet address classes are as follows:

Class A: 255.0.0.0

Class B: 255.255.0.0

Class C: 255.255.255.0

Default Gateway:  This field allows you to set an IP address for a gateway or router.  Filling in this field will allow the switching hub to know which gateway or router is responsible for the delivery of all IP packets sent by the switching hub.  This address is particularly useful if the switching hub and the network manager are not on the same network.  The default value of this parameter is 0.0.0.0, which means no gateway exists and the network are on the same network.

Up Time:  This shows how long the switching hub has been up since it was turned on or reset.

Trap Level:  This parameter is useful only if you are using PLANET’s PlanetView SNMP Network Management System.  The trap levels are proprietary to PlanetView.  This parameter allows you to select a trap level from 1 to 7.  The default trap level is 3.  For a more detailed description of the different trap levels, see Appendix E Traps.

BootP/RARP Switch:  This field allows you to enable the BootP function of the switching hub.  If you have a BootP server on your network, an IP address will be automatically mapped to the switching hub when it is first turned on.  In addition to mapping an IP address, BootP can assign the subnet mask and default gateway.  Using a BootP server avoids the trouble of having to configure devices individually.

After making the necessary changes save the settings before leaving the System Configuration menu.  For the changes to take effect it would be necessary to select the menu 7. Warm Start to restart the switching hub with the new settings.

4.2.2   Password Change

When installing the switching hub for the first time, you migExpress  hubs, you might want to use the Parallel Link feature of the hubs to increase bandwidth efficiency.  Selecting the 12.  Parallel Link menu will give you the following screen:

Picture 4-5 here

The items on the Parallel Link screen are explained as follows:

Expr wit  hub.

(2, 8) - Ports 2 and 8 are ParallelExprewit  hub.

(1, 7) (2, 8) - Ports 1, 7, 2, and 8 are PExpreSwit hub.

(1, 7) (2, 8) - Ports 1 and 7 are PaExpreSwit  hub.  Ports 2 and 8 are Parallel LinExpr Swi  hub.

Main Switch:  This field allows you to enable or disable the Parallel Link option.  Toggle the spacebar t

Set up Spanning Tree Expr wit hubs implement the spanning tree algorithm to detect and break bandwidth sapping circular traffic patterns by disabling certain links.  Implemented based on IEEE 802.1d Spanning Tree Protocol (STP), loops in redundant bridges are inhibited by maintaining the secondary bridge as backup.  If the first bridge should go down, the secondary bridge takes over.

4.4.1   Spanning Tree

To access the Spanning Tree menu, select  the 14  Spanning Tree menu from the main menu screen.  You should then see the following screen

Picture 4-6 here

The items on the Spanning Tree menu are explained as follows:

Port Number:  This is the currently selected port number.  To select another port use the caret keys “<” and “>” to move to the previous or next port number.

Bridge Priority:  This field is used to fill in a 2-octet value that allows the network manager to influence the choice of root bridge and the designated bridge.  A lower numerical value for bridge priority makes the bridge more likely to be the root.  The value range from lowest to highest is 0 to 65535.

Hello Time:  This field is used to set the time interval between issuing configuring BPDU (Bridge Protocol Data Units) which are used by the bridges to calculate a spanning tree.  The value range for this field is 100 to 1000 in 10ms units.

Max Age:  This field is used to set the time at which a configuring BPDU is discarded.  BPDU’s are stored by the switching hub in caches.  The BPDU’s are aged and discarded if no activity occurs when the aging limit is reached.  The value

Configure SNMP settings

This section talks about SNMP settings.  You will only need to read this section if you are using SNMP to manage your network.

4.5.1   Set  Device Community

Each network manager comes with community names for use to screen access rights to a particular managed device.  Only network managers having the same community names as those stored in a managed device will be allowed to receive SNMP packets from the device.

The switching hub comes with a set of default community names.  You may change any of these community names, and also set an access right (that is, read-only, or read-write) for each.  In order for the network manager to receive data from the hub, it must at least supply one of the community names that you set.  Selecting the 3.  Set Device Community from the main menu will give you the following Community Name screen:

Picture 4-7 here

The items on the Set Device Community menu screen are described as follows:

Community Name:  This field allows you to type in a community name.  You are allowed a maximum of 12 characters per community name.  To type in a community name just start typing.  Use the TAB key to go to the next field, Access Mode.  To go to the next community name use the up and down arrow keys.

Access Mode:  This field allows you to set the access right of a particular community name.  You can set this to RW (read-write) or R_Only (read-only) by toggling the spacebar key.

After making your entries, save the new entries before leaving the Set Community Name menu screen.

4.5.2   Set Trap Destination

To manage a network properly, a netw

Reset the system

After everything is done, it would be necessary to reset your switching hub to let the new settings take effect.  To reset the system using the new settings, you select the 7  Warm Start menu.

Warm Start

Selecting this menu will give you the following menu screen:

Picture 4-9 here

To reset the switching hub select the YES key to perform the reset.  To quit this menu select CANCEL to return to the main menu.

Factory Reset

This menu allows you