Virtual LANs and Filters

Virtual LANs

Virtual LANs allow you to define separate logical networks on the same switching hub by grouping ports into distinctive domains.  For example (see Figure 5-1), on your 12 port switching hub, you may group ports 1 - 7 into one domain and group ports 7 - 12 into another domain.  The effect of this is that network access Express hub are divided into two domains with a server and an FHSW-1202 present in both domains.  The server and all connections on the FHSW-1202 can therefore be accessed by workstations in both Domain 1 (LAN A) and Domain 2 (LAN B).  The FHSW-1202 also has a defined sub-domain (Domain 3).  Workstations in Domain 3 cannot access resources in Domains 1 and 2.

Figure 5-2 here

Figure 5-2  Virtual LAN (Example B)

The virtual LAN feature on PLANET hubs can be useful to a system administrator who wants to monitor different domain groups while securing them from each other.  Virtual LANs can be used to provide security by dividing ports into logical sub-networks while providing shared access to specific network resources.

To access the Virtual LAN menu select the 10. Virtual LAN sub-menu from the main menu on the console program.  You will then see the following screen:

Picture 5-1 here

You will see the following items on the screen:

Main Switch:  This field allows you to enable or disable the virtual LAN function.

Domain Switch:  This field allows you to enable or disable the domain.  Toggle the <Spacebar> to switch from enable to disable or vice-versa.

Domain No.:  This is the currently selected domain number.  Each switching hub can have a maximum of twelve (12) domains.  To move to the previous or next domain press the “<”, and “>” keys.

Port No.:  This field allows you to select the port numbers that will be in the currently defined domain.  Use the <up> and <down> arrow keys to move from port to port and use the <Spacebar> to toggle between yes or no.  Yes ports are part of the domain.

Af