Status Monitoring and Statistics

Statistics Report

You can view some statistics on the switching hub by selecting the 4.  Statistics Report sub-menu from the console program main menu screen.

The Statistics Report screens would look like the following screen:

picture 6-1 here

Each displayed statistics value is the accumulated count since the switching hub was turned on or reset.  The different fields are explained as follows:

Port Number:  This field shows the selected port on the switching hub.

There are two main sections in the Statistics Report screen.  The first section, For Unit, shows statistics for the entire hub.  The second section, For Unit, shows statistics for the selected port.  The fields in the For Unit section are explained as follows:

Total Good Frames:  This shows the total number of good frames that passed through all ports of the selected unit.  Good frames are between 64 and 1530 bytes in size with no CRC and alignment errors.

Total Good Octets:  This is the total size, in bytes, of data contained in all good frames that passed through all ports of the selected unit.

Total Errors:  This is the total number of errors that occurred on all ports of the selected unit.

Total Collisions:  This is the total number of data collisions that occurred on all segments connected to all the ports of the selected unit.

The For Port section displays statistics for the selected port (see Port Number).  The For Port fields are explained as follows:

Good Frames:  This is the total number of good frames that passed through the selected port.  Good frames are between 64 and 1531 bytes (including FCS) in size with no CRC and alignment errors.

Good Octets:  This is the total size of data contained in all good frames that passed through the selected port.

Total Errors:  This is the total number of errors that occurred on the selected port.

Collisions:  This is the total number of data collisions that occurred on the segment connected to the selected port.

Frames too Long:  This is the total number of long frames that were received on the selected port.  Long frames are those with sizes more than 1531 bytes (including FCS), with less than 5 ms duration.

Alignment Errors:  This is the total number of alignment errors detected on the selected port.  An alignment error occurs when all bytes are not received in whole.

Runts:  This is the total number of bad frames that were received on the selected port.  Runts are frames with incorrect sizes or formats that are not the result of collisions.

Last MAC Address:  This displays the MAC address of the last node that connected to the selected port.

Traffic Generator

The Traffic Generator menu allows you to generate traffic on t