Upgrading the Firmware

The switching hub firmware can be upgraded using TFTP (Trivial File Transfer Protocol).  The TFTP application is found on most TCP/IP packages.  Note that upgrading the switching hub’s firmware is done through a station connected to one of the ports on the switching hub.

The following screen examples are from NetManage Inc.’s “Chameleon” TFTP software.  When the TFTP application is accessed, you should see the following menu screen:

The following instructions show you how to upgrade the firmware using TFTP.

Select Transfer from the TFTP menu bar.  You should then see the following menu screen.

picture App2-3 here

Type the IP address of the switching hub in the Host Name field.

Type the filename for the firmware on the Remote File field.  For FE-224C switching hubs, the name of the file should read fhsw2602.bin”.

The Local Filename field should contain the name of the new firmware upgrade file.  This may be on a diskette.  Select the filename from the correct directory.

Under the Transfer Type field, select the Send option.

For Transfer Mode, select Binary.

Select OK to begin the file transfer.  The bottom half of the port LEDs will begin to cycle from Ports 1 to 6 then Ports 12 to 7.  While the firmware is downloading, the LEDs will be orange in color.  If the download was successful the LEDs would stop cycling and return to normal operating condition.  If the download was unsuccessful, then the cycling would stop and all the lower LEDs would blink continuously.