POST Diagnostics

When the switching hub is turned on for the first time, it runs a POST diagnostics routine.  The Port LEDs on the front panel would start flashing in sequence from port 1 to port 10 while the routine is running.  If an error condition occurs, the diagnostic routine would stop and  one of the Port LEDs (Ports 1 to 8) will turn red.  Red LEDs signify an error condition.  Note that green or orange LEDs signify normal operating conditions.  The switching hub will cycle through the POST routine twice if it detects an error condition the very first time that it is run.  If the error condition persists then one LED on ports 1 to 8 will light up red.  If this happens, one of the components on the switching hub might be defective - you will have to return the switching hub to your dealer to have it repaired.

The following table lists POST error details.

| LED | Error Condition |
| --- | --- |
| Port 1 |

Fail EPROM Checksum/Signature test

| Fail EPROM Device Name/Model string test |
| --- |
| Port 2 | Fail SRAM Read/Write test |
| Port 3 | Fail Management Board Diagnostics test |
| Port 4 | Fail SCC-8530 channel A/B Tx/Rx test |
| Port 5 | Fail EEPROM read/write, checksum test |
| Port 6 | Fail NIC-8019 I/O port, data port, memory test |
| Port 7 | Fail I/O (low) board diagnostics test |
| Port 8 | Fail I/O (high) board diagnostics test |
| Port 9 | Fail NuCleus setting port ID test |
| Port 10 | Fail first AMD79c981 and AMD79c987 test |
| Port 11 | Fail second AMD79c981 and AMD79c987 test |
| Port 12 | Fail third AMD79c981 and AMD79c987 test |
| Port 13 | Fail fourth AMD79c981 and AMD79c987 test |
| Port 14 | Fail Flash ROM checksum/signature, device name/model string check |
| Port 15 | Fail jump to flash code and operation test |

Table C-1 POST Error Details