Traps

This section lists the trap definitions used by PLANET’s PlanetView SNMP Network Management System.

| Level | Trap | Description |
| --- | --- | --- |
| 2 |

001

002

336

337

339

340

342

343

528

529

Become the new root of the Spanning Tree.

Spanning tree topology change.

Unit accumulated threshold is reached.

Unit rate threshold is reached.

Cluster port accumulated threshold is reached.

Cluster port rate threshold is reached.

Switching port accumulated threshold is reached.

Switching port rate threshold is reached.

Switching system channel error.

Switching port internal error.

3

256

257

272

273

288

289

530

624

625

Reset

Factory reset

Mount a unit.

Dismounted a unit.

Enable a cluster port.

Disable a cluster port.

Switching port TX CRC error.

Enable Virtual LAN function.

Disable Virtual LAN function.

Table E-1 Trap Definitions

| Level | Trap | Description |
| --- | --- | --- |
| 4 |

544

560

561

592

593

594

The address table pack-count has been changed.

The static table pack-count has been changed.

Set a collision address in the static address table.

Enable the filter function.

Disable the filter function.

Set a filter address to a switching port.

5

290

291

313

628

Port is auto-partitioned.

Port is no longer partitioned.

Source address of the node connected to a port has been changed.

Virtual LAN operation function.

6

292

293

626

627

Link state of a port has been changed from down to up.

Link state of a port has been changed from up to down.

Virtual LAN function is activated on the specific port.

Virtual LAN function is removed from the specific port.

Table E-1 Trap Definitions(continued)