Virtual LANs and Filtering

Virtual LANs

Virtual LANs allow you to define separate logical networks on the same switching hub by grouping switching ports into distinctive domains.  For example, on your FHSW-2602 switching hub, you may group Ethernet segments 1 and 2 (ports 1 - 6, 7 - 12) and port P1 into one domain and segments 3 and 4 (ports 13 - 18, 19 - 24) and ports P1 and P2 into another domain.  The effect of this is that access is restricted to the ports in the same domain.  A switching port may be in more than one domain.  In this example port P1 is in both domains.  Switching ports on both domains can therefore access port P1 which may be connected to a server or another switching hub.

figure 5-1 here

Figure 5-1  Virtual LAN (Example A)

The virtual LAN feature on PLANET hubs can be useful to a system administrator who wants to monitor different domain groups while securing them from each other.  Virtual LANs can be used to provide security by dividing switching ports into logical sub-networks while providing shared access to specific network resources.

figure 5-2 here

Figure 5-2  Virtual LAN (Example B)

To access the Virtual LAN menu select the 12.  Virtual LAN sub-menu from the main menu on the console program.  You will then see the following screen:

picture 5-1 here

You will see the following items on the screen:

| Menu Option | Description |
| --- | --- |
| Main Switch | This field allows you to enable or disable the virtual LAN function. |
| Domain No. | This is the currently selected domain number. Each switching hub can have a maximum of twelve (12) domains. To move to the previous or next domain press the "<" and ">" keys. |
| Port No. | This field allows you to select the switching port numbers that will be in the currently defined domain. Use the <up> and <down> arrow keys to move from switching port to switching port and use the <Spacebar> to toggle between yes or no. Yes ports are part of the domain. |

After defining your domains, save your settings before leaving the menu.

Note:  If you have already defined domains in your virtual LAN please avoid moving workstation connections from one port to another.  The switching hub has learned the MAC addresses of the individual workstations connected to the virtual LAN ports.  If moving workstation connections is unavoidable perform a warm start (7.  Warm Start) on the switching hub to allow the hub to relearn the new MAC addresses.

Filtering

Filtering allows you, the network administrator, to restrict specific MAC addresses from accessing the port.  A total of thirty two (32) MAC addresses per port can be filtered out.

Note:  The Filtering and Virtual LAN functions cannot be both enabled at the same time.  If both are enabled, Virtual LAN will take precedence over Filter.

To set filtering, select the 13. Filtering sub-menu from the console program main menu screen.  You will then see the following screen:

picture 5-2 here

The items on the menu are described as follows:

| Menu Option | Description |
| --- | --- |
| Port No. | This is the currently selected switching port number. To select another port use the caret keys “<” and “>” to move to the previous or next switching port number. |
| Filtering Main Switch | This is the main switch that enables or disables filtering for all the ports on the switching hub. Use the <Spacebar> to toggle between ON and OFF. |
| Filtering Source Address | This allows you to type in the specific MAC addresses of the nodes that should be filtered or prevented from accessing the port. You can enter a maximum of 32 MAC addresses. |

After making your entries, save the new entries before leaving the Filtering menu screen.