REGULATORY STATEMENTS

FCC Certification

The United States Federal Communication Commission (FCC) and the Canadian Department of Communications have established certain rules governing the use of modems and other electronic equipment.

FCC Part 68 Registration

The high speed FAX/MODEM is registered with the FCC as compliant with the rules of Part 68, and use of this modem is subject to the following restrictions:

1. The Federal Communication Commission FCC has established rules which permit this device to be directly connected to the telephone network. Standardized jacks are used for these connections. This equipment should not be used on party lines or coin phones.

2. If this device is malfunctioning, it may also be causing harm to he telephone network; this device should be disconnected until the source of the problem can be determined and until repair has been made. If this is not done, the telephone company may temporarily disconnect service.

3. The telephone company may make changes in it’s facilities, equipment, operation and procedures; if such changes affect the compatibility or use of this device, the telephone company is required to give adequate notice of the with the FCC.

4. If the telephone company requests information on what equipment is connected to their lines, inform them of:

a. The telephone number which this unit is connected to

b. The ringer equivalence number.

c. The USOC jack required.

d. The FCC Registration number.

Items (b) and (d) are indicated on the label. The Ringer Equivalence Number (REN) is used to determine how many devices can be connected to your telephone line. In most areas, the sum of the REN’s of all the devices on any one line should not exceed 5.0. If too many devices are attached, they may not ring properly.

FCC Part 15 Registration

This modem complies with Part 15 of FCC rules. Operation is subject to the following two conditions:

1) This device may not cause harmful interface, and

2) this device must accept any interface received, including interface that may cause undesired operation.

This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to Part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses and can radiate radio frequency energy, and if not installed and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna.

- Increase the distance between the equipment and receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

- Consult an experienced radio/TV technician for help.

CTR 21 pan-European Certification

This equipment has been approved in accordance with Council Decision 98/482/EC for pan-European single terminal connection to the public switched telephone network (PSTN). However, due to differences between the individual PSTNs provided in different countries, the approval does not, of itself, give an unconditional assurance of successful operation on every PSTN network termination point. In the event of problems, you should contact your equipment supplier in the first instance.

This device is designed to work with the notified networks in all EC member states. Nevertheless, some of the network services in invidual countries might not be supported, but they will not affect the normal data and fax applications. For example, the metering charge service in Germany. Besides you may encounter difficulty of using PULSE dialing function in some of the countries, such as Nordic countries. This kind of network compatibility is dependent on the physical and software settings of this device.  If the users are desired to use this device on those networks, they should contact the vendor or supplier first.

Reversion

This user's guide is for PLANET Fax/Modem family, model:

ME-560R 56K External Fax/Modem

Rev. 1.0 (January, 99)

Part No.: EM-ME560R

Table of Content

GETTING STARTED MANUAL	4

The LED Indicators on the Front Panel	4

The Rear Panel and the Connectors	5

The Serial Port and the RS-232 Cable	6

Hardware Connection	6

Test the Power Connection	7

Test the Telephone Line Connection	7

Data Communications Software Packages	7

Fax Communications Software Packages	7

Error-Correction and Data Compression	7

Controlling the Modem Speaker	8

The Modem Commands	9

Prefix, Repeat and Escape Commands	9

Dial Commands and Dial Modifiers	9

Operation Commands	9

V.42bis and MNP Commands	11

Voice Commands for Rockwell Chip Set	13

Fax Class I Commands	13

Fax Class II Commands	14

S-Register Summary	15

Result Codes	16

Installation of Modem Driver in Windows 95	19

# GETTING STARTED MANUAL

If you will use this modem with a personal computer and a popular off-the-shelf communications software, for a simple modem application such as going on-line with bulletin boards system (BBS), up-loading or downloading files, and sending fax messages, you may now go to the Getting Started Manual to exercise hardware connection for your modem. Then, you should refer to your software’s manual to get on the road. This manual will serve as your guide for modem commands.

If you would like to know the modem operations and commands in more depth, the Electronic Manual of Fax-modem diskette is included to serve this purpose.

## The LED Indicators on the Front Panel

The indicators on the modem’s front panel denote the current modem operation characteristics and status. They are:

| MR | Modem Ready. Lights up when the modem is turned on. |
| --- | --- |
| TR | Terminal Ready. Flashes when DTR signal is detected. |
| CD | Carrier Detected. Lights up when a carrier from the remote modem is detected. |
| SD | Send Data. Flashes when the modem is sending data to the remote modem or when receiving data from the local computer. |
| RD | Receive Data. Flashes when the modem is receiving data from the remote modem or when sending data to the local computer. |
| AA | Auto-Answer. Lights up when the modem is set for auto-answer. Flashes when an incoming ring is detected. |
| OH | Off-Hook. Lights up when the modem is using the telephone line. Off when the modem hangs-up (on-hook). |
| HS | High Speed. Lights up when modem speed exceeds 4800 bps. When you turn on your modem, at least the MR indicator shall light up. There may be some other indictors lights depended on the settlement of the modem. Otherwise, you should check the power connected to your modem. |

## The Rear Panel and the Connectors

PHONE	：Accepts a telephone set connected parallel to your modem.

LINE	：Accepts the RJ-11 cable that links your modem to a telephone line or to a 2-wire leased-line.

RS-232	：Accepts the serial cable that is connected between your modem and your computer.

12VAC	：Accepts the power adapter that comes with your modem.

## The Serial Port and the RS-232 Cable

To use this modem, it will require an RS-232 serial port on your computer. If your do not have it, you need to have one.

It is better to select a serial port card that uses a high-speed 16550 UART chip. A card with an ordinary UART chip handles transmissions at a maximum speed around 38,400bps. In case the data compression of your modem is active, it may perform at an exceeding speed and an ordinary serial port card may sometimes cause data loss.

You will also require an RS-232 cable to connect your modem with computer. You will be Asked to buy a modem cable if you are a PC user. The modem cable shall, at one end, have a DB25M (male) connector that fits the female connector on the modem, and at the other end a serial port connector that matches your computer.

## Hardware Connection

1) Make sure that both the modem and computer are turned off.

2) Use an RS-232 cable to connect the modem to a serial port on your computer. Secure the connector screw on it.

(  Verify the serial port number in which your modem is connected. You must Write down the port number as you will need to specify this number during software installation. As a general rule on PC applications, the port COM1 is connected to a mouse, while COM2 is for a modem.

3) Use an RJ-11 cable to connect the LINE jack to the wall outlet of the telephone line.

4) Connect a telephone set to the PHONE jack. You may leave this jack disconnected if desired.

5) Make sure that the power adapter that comes with your modem is of a correct voltage that complies with your power source. Use the adapter to connect the power source to the 12VAC jack on the modem.

## Test the Power Connection

You can turn on your modem by pushing the power switch button and watch the front panel indicators. Depending on the setting of your modem, the MR and other indicators should light up. If none is lit, check the power connection for the modem.

## Test the Telephone Line Connection

Once a telephone set is connected, you may test the line quality and connections by lifting the telephone handset, listening for a clear dial tone, and making several telephone calls. The calls shooed go through well and the sound loud and clear. Otherwise, the line may be poor or have a faulty connection.

## Data Communications Software Packages

Your modem follows the industrial standard in the modem command set. As a result, most of the popular communications software packages off-the-shelf will work with it. You should select a software package according to your application requirement.

Most popular communications software is provided with the configuration named Initial-String or Dialing-Prefix. It is wise to check, one by one, the commands in this string, as they will be sent to determine the modem characteristics each time prior to dialing.

## Fax Communications Software Packages

Similar to data communication applications, you interact with the modem through the fax communications software.

Your modem only supports Class 1 command set.

## Error-Correction and Data Compression

Your modem supports the industrial standards of MNP 5 and ITU-T (formerly called CCITT) V.42bis for error-correction and data compression (ECDC). Both standards are capable of error-correction as well. The modem will re-transmit a faulty data block when an error is detected while receiving.

The ITU-T V.42bis can perform data compression at a rate up to four times, depending on the format of data. That is, the throughput can be reach as high as 57,600 bits per second when you are on-line at 14,400bps.

The MNP 5 was popular before V.42bis was born. It can reach a compression rate of two times that is around half of what V.42bis can do.

To enjoy the effectiveness of ECDC, both modems on-line should exercise the same ECDC standard. You should always set your modem to V.42bis auto-reliable mode by command \N3, which will automatically negotiate with the remote modem for an available ECDC standard.

## Controlling the Modem Speaker

In the factory, your modem speaker is preset in to medium volume and turned on when the carrier from the remote modem is detected. You may issue the commands L and M, with an appropriate parameter following it, to control the volume, or turn on the speaker.

# The Modem Commands

## Prefix, Repeat and Escape Commands

AT	Attention. Precede all command lines except A/ and +++

A/	Re-execute the last command in command buffer

+++	Escape characters, requires guard time before and after

## Dial Commands and Dial Modifiers

D	Originate a call

S=n	Dial the nth stored number

T	Touch tone dialing

P	Pulse dialing

R	Dial in answer mode

W	Wait for second dial tone

L	Re-Dial the last valid telephone number

,	Pause

!	Flash

;	Return to command state

## Operation Commands

A	Answer incoming call

B0	CCITT or ITU-T compatibility

B1	Bell protocol only

E0	Disable command echo

E1	Enable echo command characters

H0	Hang up the connection (on-hook)

H1	Go off-hook to make a call

I0	Reports product code

I1	Calculates the ROM checksum

I3	Reports firmware version

L0	Low volume

L1	Low volume

L2	Medium volume

L3	High volume

M0	Speaker off at all times

M1	Speaker on until CD detected

M2	Speaker always on

N0	Fixed data rate follow *N command

N1	Enable adaptive data rate

O0	Return to data-link without retrain

O1	Return to data-link with retrain

Q0	Modem sends response codes

Q1	Do not send response codes

Sr?	Display the value in register r

Sr=n	Set register r to a value n

V0	Display response codes in digit form

V1	Display response codes in words

W0	Disable V.42 response codes, display DTE speed

W1	Enable V.42 response codes, display DCE speed

W2	Disable V.42 response codes, display DCE speed

X0	Enable basic response codes 0-4

X1	Do not detect dial tone and busy signal

X2	Include dial tone detection response

X3	Include busy detection response

X4	Enable all response codes

Y0	Do Not send (and ignore) break signal

Y1	Send break signal for 4 seconds before disconnect

Z0	Reset modem with SCP0

Z1	Reset modem with SCP1

&C0	Turn CD signal to always on

&C1	CD on at remote carrier detected

&D0	Alone with any of following &Q0, &Q5, &Q6 then, DTR is not functional.

Alone with any of following &Q1, &Q4 then DTR drop causes the modem hang up, Auto-answer is not affected.

Alone with any of following &Q2, &Q3 DTR drop causes the modem to hang up, Auto-Answer is inhibited

&D1	Alone with any of following &Q0, &Q1, &Q4, &Q5, &Q6 DTR drop is interpreted by the modem as if the asynchronous escape sequence had been entered. the modem returns to asynchronous Command State without disconnecting.

Alone with any of following &Q2, &Q3 DTR drop causes the modem to hang up. Auto-Answer is inhibited.

&D2	Alone with any of following &Q0 through %Q6 then, DTR drop causes the modem to hang up Auto-Answer is inhang.

&D3	Alone with any of following &Q0, &Q1, &Q4, &Q5, &Q6 DTR drop causes the modem to perform a soft-reset as if the z command were received. The &Y setting determines which profile is loaded.
Alone with any of following &Q2, &Q3 DTR drop causes the modem to hang up Auto-Answer is inhibited.

&F0	Restore factory default profile FDP0 (as ECDC modem)

&F1	Restore factory default profile FDP1 (as non-ECDC modem)

&G0	Disable guard tone

&G1	Disable guard tone (default for us models)

&G2	Enable 1800 Hz guard tone

&Ln	Leased line dail line operation

&L0	Dial-Up line operation

&G2	Leased line operation

&K0	Disable flow control

&K3	RTS/CTS flow control

&K4	XON/OFF flow control

&K5	Unidirectional XON/OFF

&K6	RTS/CTS, XON/XOFF flow control

&M0	Set modem for async operation

&M1	Enter sync mode after async dialing

&M2	Sync terminal support. Modem dials a stored number and enters sync mode when DTR off-to-on

&M3	Dial manually while DTR off, handshake proceeds when DTR off-to-on

&P0	M/B ratio 39/61(USA)

&P1	M/B ratio 33/67(UK, Hong Kong)

&P2	M/B ratio 39/61 at 20 pulses

&P3	M/B ratio 33/67 at 20 pulses

&Q0	See & M0

&Q1	See & M1

&Q2	See & M2

&Q3	See & M3

&Q4	Selects Auto Sync operation. When used in conjunction with the Hayes synchronous interface (HCI)capability in the DTE. Provides synchronous communication capability from an asynchronous terminal

&Q5	The modem will try to negotiate an error-corrected link

&Q6	Select asynchronous operation in normal mode

&R0	Modem turns CTS on when detects RTS from the local computer

&R1	Ignore RTS. Modem turns CTS on when ready to receive synchronously

&S0	Modem forces DSR always on

&S1	Set DSR to follow RS-232 spec

&T0	Terminates test in progress

&T1	Initiates local analog loopback, V.34 Loop3, Sets S16 bit0. If aconnect exists when this command is issued, the modem hangsup, The connect xxxx message is displayed upon the start of the test.

&T5	Disable digital loopback acknowledgment for remote request.

&T8	Initiates local analog loopback, V.34 Loop3, with selftest.

&V	Display modem profiles and numbers

&W0	Write ACP to SCP0

&W1	Write ACP to SCP1

&X0	Select internal clock

&X1	Select external clock

&X2	Select slave clock

&Y0	Designate SCP0 as the active SCP

&Y1	Designate SCP1 as the active SCP

&Zn=	Save up to three numbers to NVRAM. Use DS=n to dial the stored number

Note: &Q,&M: for Sync mode only

## V.42bis and MNP Commands

\A0	MNP block size 64 characters

\A1	MNP block size 128 characters

\A2	MNP block size 192 characters

\A3	MNP block size 256 characters

\Bn	Send n/10 seconds of line break to the modem (n = 0 ~ 9, default 3)

\K0	Enter command mode, do not send a break signal to remote (To send a break after use the \B command)

\K1	Clear data buffer and send a break

\K2	Same as \K0

\K3	Immediately send a break

\K4	Same as \K0

\K5	Send a break in sequence with any data received from the port

\N0	Set modem to normal mode

\N1	Set modem to direct mode

\N2	Set modem to MNP reliable mode

\N3	Set to MNP/V.42 auto-reliable mode

\N4	V.42 reliable with phase detection

\V0	Connect messages are controlled by the command settings X, W, and S95.

\V1	Connect message displayed in the single line format described below subject to the command settings V (Verbose) and Q(Quiet). In Non-Verbose mode(V0), single line connect messages are disabled and a single numeric result code is generated for CONNECT DTE.

%C0	Disable data compression

%C1	Enable MNP5 data compression negotiation

%C2	Enable V.42bis data compression

%C3	Enable both V.42bis and MNP5 data compression (default)

%E0	Disable auto-retrain

%E1	Enable auto-retrain

%E2	Enable fallback/fall forward

## Voice Commands for Rockwell Chip Set

The Voice Command

| Command | Function |
| --- | --- |
| A | Answering in Voice/Audio Mode |
| D | Dial command in Voice/Audio Mode |
| H | Hang up in Voice/Audio Mode |
| Z | Reset from Voice/Audio Mode |
| #BDR=n | Select baud rate (turn off autobaud) 0<n<48 |
| #CID=n | Enable Caller ID detection and select reporting format n=0~2 |
| #CLS=n | Select data, fax, or Voice/Audio n=0,1,2,8 |
| #MDL? | Identify model |
| #MFR? | Identify manufacturer |
| #REV? | Identify revision level |
| #TL | Audio output transmit level |
| #VBQ? | Query buffer size |
| #VBS=n | Bits per sample (ADPCM or PCM) n=2,4,8 |
| #VBT=n | Beep tone timer n =0~40 (0-4 seconds) |
| #VCI? | Identify compression method (ADPCM) |
| #VLS=n | Voice line select (ADPCM or PCM) n=@~9 |
| #VRA | Ringback goes away timer (originate) |
| #VRN | Ringback never came timer (originate) |
| #VRX | Voice Receive Mode (ADPCM or PCM) |
| #VSD | Enable silence deletion (voice receive, ADPCM) |
| #VSK=n | Buffer skid setting n=255 |
| #VSP | Silence detection period (voice receive, ADPCM) |
| #VSR | Sampling rate selection (ADPCM or PCM) |
| #VSS | Silence detection tuner (voice receive, ADPCM) |
| #VTD | DTMF tone reporting capability |
| #VTM | Enable timing mark placement |
| #VTS | Generate tone signals |
| #VTX | Voice transmit mode (ADPCM or PCM) |

## Fax Class I Commands

| Command | Function |
| --- | --- |
| Service Class ID |
| +FCLASS= | Service Class |
| Fax Class 1 Commands |
| +FAE=n | Data/Fax auto Answer |
| +FTS=n | Stop Transmission and Wait |
| +FRS=n | Receive Silence |
| +FTM=n | Transmit Data |
| +FRM=n | Receive Data |
| +FTH=n | Transmit Data with HDLC Framing |
| +FRH=n | Receive Data with HDLC Framing |

## Fax Class II Commands

| Command | Function |
| --- | --- |
| +FCLASS=n | Service class |
| +FAA=n | Adaptive answer |
| +FAXERR | Fax error value |
| +FBOR | Phase C data bit order |
| +FBUF? | Buffer size (read only) |
| +FCFR | Indicate confirmation to receive |
| +FCLASS= | Service class |
| +FCON | Facsimile connection response |
| +FCIG | Set the polled station identification |
| +FCIG: | Report the polled station idendification |
| +FCR | Capability to receive |
| +FCR= | Capability to receive |
| +FCSI: | Report the called station ID |
| +FDCC= | DCE capabilities parameters |
| +FDCS: | Report current session |
| +FDCS= | Current session results |
| +FDIS: | Report remote capabilities |
| +FDIS= | Current sessions parameters |
| +FDR | Begin or continue phase C receive data |
| +FDT= | Data transmission |
| +FDTC: | Report the polled station capabilities |
| +FET: | Post page message response |
| +FET=N | Transmit page punctuation |
| +FHNG | Call termination with status |
| +FK | Session termination |
| +FLID= | Local ID string |
| +FLPL | Document for polling |
| +FMDL? | Identify model |
| +FMFR? | Identify manufacturer |
| +FPHCTO | Phase C time out |
| +FPOLL | Indicates polling request |
| +FPTS: | Page transfer status |
| +FPTS= | Page |
| +FREV? | Identify revision |
| +FSPL | Enable polling |
| +FTSI: | Report the transmit station ID |

## S-Register Summary

| Register | Range | Units | Default | Function |
| --- | --- | --- | --- | --- |
| S0 | 0-255 | Rings | 0 | Rings to Auto-Answer |
| S1 | 0-255 | Rings | 0 | Rings Counter |
| S2 | 0-255 | ASCII | 43 | Escape character |
| S3 | 0-127 | ASCII | 13 | Carriage return character |
| S4 | 0-127 | ASCII | 10 | Line Feed Character |
| S5 | 0-255 | ASCII | 8 | Backspace character |
| S6 | 2-255 | s | 2 | Wait Time for Dial Tone |
| S7 | 1-255 | s | 50 | Wait Time for Carrier |
| S8 | 0-255 | s | 2 | Pause Time for Dial Delay Modifier |
| S9 | 1-255 | 0.1s | 6 | Carrier Detect Response Time |
| S10 | 1-255 | 0.1s | 14 | Carrier Loss Disconnect Time |
| S11 | 50-255 | 0.001s | 95 | DTMF Tone Duration |
| S12 | 0-255 | 0.02s | 50 | Escape Prompt Delay |
| S13 | - | - | - | Reserved |
| S14 | - | - | 138(8Ah) | General Bit Mapped Options Status |
| S15 | - | - | - | Reserved |
| S16 | - | - | 0 | Test Mode Bit Mapped Options Status(&T) |
| S17 | - | - | - | Reserved |
| S18 | 0.255 | s | 0 | Test Timer |
| S19 | - | - | 0 | AutoSync Options |
| S20 | 0-255 | - | 0 | AutoSync HDLC Address or BSC Sync Character |
| S21 | - | - | 52(34h) | V.24/General Bit Mapped Options Status |
| S22 | - | - | 117(75h) | Speaker/Results bit Mapped Options Status |
| S23 | - | - | 62(3Dh) | General Bit Mapped Options Status |
| S24 | 0-255 | s | 0 | Sleep Inactivity Timer |
| S25 | 0-255 | s or 0.01s | 5 | Delay to DTR Off |
| S26 | 0-255 | 0.01s | 1 | RTS-to-CTS Delay |
| S27 | - | - | 73(49h) | General Bit Mapped Options Status |
| S28 | - | - | 0 | General Bit Mapped Options Status |
| S29 | 0-255 | 10ms | 70 | Flash Dial Modifier Time |
| S30 | 0-255 | 10s | 0 | Disconnect Inactivity Timer |
| S31 | - | - | 194(C2h) | General Bit Mapped Options Status |
| S32 | 0-255 | ASCII | 17(11h) | XON Character |
| S33 | 0-255 | ASCII | 19(13h) | XOFF Character |
| S34-S35 | - | - | - | Reserved |
| S36 | - | - | 7 | LAPM Failure Control |
| S37 | - | - | 0 | Line Connection Speed |
| S38 | 0-255 | s | 20 | Delay Before Forced Hang-up |
| S39 | - | - | 3 | Flow Control Bit Mapped Options Status |
| S40 | - | - | 104(68h) | General Bit Mapped Options Status |
| S41 | - | - | 195(C3h) | General Bit Mapped Options Status |
| S42-S45 | - | - | - | Reserved |
| S46 | - | - | 138 | Data Compression Control |
| S48 | - | - | 7 | V.42 Negotiation Control |
| S82 | - | - | 128(40h) | LAPM Break Control |
| S86 | 0-255 | - | - | Call Failure Reason Code |
| S91 | 0-15 | dBm | 10(country dependent) | PSTN Transmit Attenuation Level |
| S92 | 0-15 | dBm | 10(country dependent) | Fax Transmit Attenuation Level |
| S95 | - | - | 0 | Result Code Messages Control |
| Register value may be stored in one of two user profiles with the &W command. |

## Result Codes

|  |  | n Value in ATXn Command |  |
| --- | --- | --- | --- |
|  |  | 0 | 1 | 2 | 3 | 4 |  |
| 0 | OK | x | x | x | x | x | Note 2 |
| 1 | Connect | x | x | x | x | x |  |
| 2 | Ring | x | x | x | x | x |  |
| 3 | No Carrier | x | x | x | x | x |  |
| 4 | Error | x | x | x | x | x |  |
| 5 | Connect 1200 | 1 | x | x | x | x |  |
| 6 | No dial tone | 3 | 3 | x | x | x |  |
| 7 | Busy | 3 | 3 | 3 | x | x |  |
| 8 | No Answer | x | x | x | x | x |  |
| 9 | Connect 600 | 1 | x | x | x | x |  |
| 10 | Connect 2400 | 1 | x | x | x | x |  |
| 11 | Connect 4800 | 1 | x | x | x | x |  |
| 12 | Connect 9600 | 1 | x | x | x | x |  |
| 13 | Connect 7200 | 1 | x | x | x | x |  |
| 14 | Connect 12000 | 1 | x | x | x | x |  |
| 15 | Connect 14400 | 1 | x | x | x | x |  |
| 16 | Connect 19200 | 1 | x | x | x | x |  |
| 17 | Connect 38400 | 1 | x | x | x | x |  |
| 18 | Connect 57600 | 1 | x | x | x | x |  |
| 19 | Connect 115200 | 1 | x | x | x | x |  |
| 20 | Connect 230400 | x | x | x | x | x | Note 2 |
| 22 | Connect 75TX/1200RX | 1 | x | x | x | x |  |
| 23 | Connect 1200TX/75RX | 1 | x | x | x | x |  |
| 24 | Delayed | 4 | 4 | 4 | 4 | x |  |
| 32 | Blacklisted | 4 | 4 | 4 | 4 | x |  |
| 33 | Fax | x | x | x | x | x |  |
| 35 | Data | x | x | x | x | x |  |
| 40 | Carrier 300 | x | x | x | x | x |  |
| 44 | Carrier 1200/75 | x | x | x | x | x |  |
| 45 | Carrier 75/1200 | x | x | x | x | x |  |
| 46 | Carrier 1200 | x | x | x | x | x |  |
| 47 | Carrier 2400 | x | x | x | x | x |  |
| 48 | Carrier 4800 | x | x | x | x | x |  |
| 49 | Carrier 7200 | x | x | x | x | x |  |
| 50 | Carrier 9600 | x | x | x | x | x |  |
| 51 | Carrier 12000 | x | x | x | x | x |  |
| 52 | Carrier 14400 | x | x | x | x | x |  |
| 53 | Carrier 16800 | x | x | x | x | x |  |
| 54 | Carrier 19200 | x | x | x | x | x |  |
| 55 | Carrier 21600 | x | x | x | x | x |  |
| 56 | Carrier 24000 | x | x | x | x | x |  |
| 57 | Carrier 26400 | x | x | x | x | x |  |
| 58 | Carrier 28800 | x | x | x | x | x |  |
| 59 | Connect 16800 | 1 | x | x | x | x |  |
| 61 | Connect 21600 | 1 | x | x | x | x |  |
| 62 | Connect 24000 | 1 | x | x | x | x |  |
| 63 | Connect 26400 | 1 | x | x | x | x |  |
| 64 | Connect 28800 | 1 | x | x | x | x |  |
| 66 | Compression: Class 5 | x | x | x | x | x |  |
| 67 | Compression: V.42bis | x | x | x | x | x |  |
| 69 | Compression: None | x | x | x | x | x |  |
| 70 | Protocol: None | x | x | x | x | x |  |
| 77 | Protocol: LAPM | x | x | x | x | x |  |
| 78 | Carrier 31200 | x | x | x | x | x |  |
| 79 | Carrier 33600 | x | x | x | x | x |  |
| 80 | Protocol: ALT | x | x | x | x | x |  |
| 81 | Protocol: ALT-Cellular | x | x | x | x | x |  |
| 84 | Connect 33600 | 1 | x | x | x | x |  |
| 91 | Connect 31200 | 1 | x | x | x | x |  |
| 150 | Carrier 32000 | x | x | x | x | x | Note 2 |
| 151 | Carrier 34000 | x | x | x | x | x | Note 2 |
| 152 | Carrier 36000 | x | x | x | x | x | Note 2 |
| 153 | Carrier 38000 | x | x | x | x | x | Note 2 |
| 154 | Carrier 40000 | x | x | x | x | x | Note 2 |
| 155 | Carrier 42000 | x | x | x | x | x | Note 2 |
| 156 | Carrier 44000 | x | x | x | x | x | Note 2 |
| 157 | Carrier 46000 | x | x | x | x | x | Note 2 |
| 158 | Carrier 48000 | x | x | x | x | x | Note 2 |
| 159 | Carrier 50000 | x | x | x | x | x | Note 2 |
| 160 | Carrier 52000 | x | x | x | x | x | Note 2 |
| 161 | Carrier 52000 | x | x | x | x | x | Note 2 |
| 162 | Carrier 56000 | x | x | x | x | x | Note 2 |
| 165 | Connect 32000 | x | x | x | x | x | Note 2 |
| 166 | Connect 34000 | x | x | x | x | x | Note 2 |
| 167 | Connect 36000 | x | x | x | x | x | Note 2 |
| 168 | Connect 38000 | x | x | x | x | x | Note 2 |
| 169 | Connect 40000 | x | x | x | x | x | Note 2 |
| 170 | Connect 42000 | x | x | x | x | x | Note 2 |
| 171 | Connect 44000 | x | x | x | x | x | Note 2 |
| 172 | Connect 46000 | x | x | x | x | x | Note 2 |
| 173 | Connect 48000 | x | x | x | x | x | Note 2 |
| 174 | Connect 50000 | x | x | x | x | x | Note 2 |
| 175 | Connect 52000 | x | x | x | x | x | Note 2 |
| 176 | Connect 54000 | x | x | x | x | x | Note 2 |
| 177 | Connect 56000 | x | x | x | x | x | Note 2 |
| +F4 | +FCERROR | x | x | x | x | x |  |
| Notes: An “x” in a column indicates that the message (either the long form if verbose, or the value only for short form) will be generated when that particular value of “n” (shown at the top of the column) has been selected by the use of ATXn. If the (verbose or short form) will be output for that X option. |

# Installation of Modem Driver in Windows 95

(1). Turn on computer. Move mouse to “Start” at left hand side, enter “Setting-s” and select “Control panel”.

(2). Under “Control Panel” select “Modems”. (or Move mouse to “My computer” at right hand side, enter “Control panel and Modems”.)

(3) In Install New Modem, please tick “Don‘t detect my modem; I will select it from a lost”, and then go to next step.

(4) Because the modem is not listed, you click “Have Disk” for other modem models.

(5) Insert the installation disk into the driver selected, click “Browse”, select one of the inf files (modem.inf for modem products), and then click “OK”.

(6) Click the manufacturer and model of your modem, and then go to next step.

(7) Select the port to use with this modem, for example COM2, and then click “Next”.

(8) Your modem has been set up successfully. Click “Finish”.

(9) Select the modem you have, and then click “OK”.

# Text boxes

RS-232

Line Phone

To Serial Port on your Computer

Connect to Telephone Line

Long Form

Short Form

Notes

Power Adaptor

Connect to Telephone Set

Power